## Slide 1: Analog-to-Digital Converter
Razvan Bogdan Embedded Systems

## Slide 2: Content
Basics of A/D Conversion
The HCS12 A/D Converter
Registers Related to A/D Converters
Procedure for Performing A/D Conversion
Temperature Sensor TC1047A
The Humidity Sensor IH-3606
The SenSym ASCX30AN Pressure Sensor
Digital to Analog Converter

## Slide 3
Basics of A/D Conversion
Many embedded systems need to deal with nonelectric quantities: weight, humidity,
pressure, weight, mass or airflow, temperature, light intensity, and speed.
These nonelectric quantities are analog in nature.
Analog quantities must be converted into digital format so that they can be processed by
the computer.
An A/D converter can only deal with electric voltage.
Any nonelectric quantity must be converted into an electric quantity using certain type
of transducer.
A transducer converts a nonelectric quantity into an electric quantity.
The output of a transducer may not be in a suitable range for A/D conversion.
A signal conditioning circuit is needed to shift and scale the transducer output to a range
suitable for A/D conversion.

## Slide 4
Analog Voltage and Digital Code Characteristic
An ideal A/D converter should have an characteristic as shown in Figure 12.2.
An A/D converter with characteristic as shown in Figure 12.2 would need
infinite number of bits to represent the A/D conversion result.

## Slide 5
An n-bit A/D converter has 2n possible output code values.
The output characteristic of an n-bit A/D ideal converter is shown in Figure 12.3.
The area above and below the dotted line is called quantization error.
Using n-bit to represent A/D conversion has an average error of 2n+1.
A real A/D converter output may have nonlinearity and non-monotonicity errors.
Analog Voltage and Digital Code Characteristic

## Slide 6
Parallel (Flash) A/D conversion
2n comparators are used
One input to each comparator is the voltage to be converted.
The second input to each comparator is the voltage that represents one of the 2n
combinations.
The comparator output will be high if the analog input is higher than the voltage that
represents one of the 2n combinations.
The largest n-bit value that causes the comparator output to become true is selected
as the A/D conversion value.
The conversion speed is very fast.
The drawback is cost.
Major applications are those that require high speed but low resolution.
Slope and Double-Slope A/D Converters
Use capacitors’ charging and discharging behavior to perform A/D conversion.
Requires only simple hardware and is popular in low-speed applications.
Has been used in Microchip PIC14400 family microcontrollers.
A/D Conversion Algorithms

## Slide 7
Sigma-Delta A/D Converters
Use over-sampling technique to perform A/D conversion.
Has good noise immunity and can achieve high resolution
Popular in high-resolution applications
Performance becomes acceptable with the advancement in CMOS technology
Successive Approximation Method
Approximates the analog signal in n steps.
The first step initializes the SAR register to 0.
Performs a series of guessing steps that starts from the most significant bit and proceeding
toward the least significant bit.
For every bit in SAR register guess it to be 1.
Converts the value of the SAR register to analog voltage.
Compares the D/A output with the analog input and clears the bit to 0 if the D/A output
is larger.
A/D Conversion Algorithms

## Slide 8
A/D Conversion Algorithms

## Slide 9
Needs a low reference voltage (VRL) and a high reference voltage (VRH) in performing
A/D conversion.
VRL is often set to ground level.
VRH is often set to VDD.
Most A/D converter are ratiometric, i.e.,
(a) A 0 V (or VRL) analog input is converted to the digital code of 0.
(b) A VDD (or VRH) analog input is converted to the digital code of 2n – 1.
(c) A k-V input will be converted to the digital code of k  (2n – 1)  VDD.
The A/D conversion result will be the most accurate if the value of analog signal covers
the whole voltage range from VRL to VRH.
The A/D conversion result k can be translated back to an analog voltage VK by the
following equation:
VK = VRL + (range  k)  (2n – 1)
Optimal Voltage Range for A/D Conversion

## Slide 10
Some of the transducer output voltage are in the range of 0 ~ VZ, where VZ < VDD.
VZ can be much smaller than VDD.
When VZ is much smaller than VDD, the A/D conversion result cannot be accurate.
The solution to this problem is to use an scaling circuit to amplify the transducer output
to cover the whole range of 0 V to VDD.
AV = VOUT  VIN = (R1 + R2)  R1
= 1 + R2/R1
Example 12.2 Choose appropriate values of R1 and R2 in Figure 12.6 to scale a voltage
in the range of 0~200mV to 0~5V.
Solution: AV = 1 + R2/R1 = 5V / 200mV = 25
R2/R1 = 24
Choose R1 = 10 KOhm and R2 = 240 KOhm to achieve the desired ratio.
Scaling Circuit

## Slide 11
Some transducer has output voltage in the range from V1 to V2 (V2 > V1).
The accuracy of the A/D conversion will be more accurate if this voltage can be
scaled and shifted to 0 ~ VDD.
The circuit shown in Figure 12.7 can shift and scale the voltage from V1 to V2 to the
range of 0~VDD.
Voltage Translation Circuit
Example 12.3 Choose appropriate resistor values and the adjusting voltage so that the circuit shown in Figure 12.7c can shift the voltage from the range of –1.2 V ~ 3.0 V to the range of 0V ~ 5V.
Solution: Applying Equation 12.5:
0 = -1.2  (Rf/R1) – (Rf/R2)  V1
5 = 3.0  (Rf/R1) – (Rf/R2)  V1
By choosing R0 = R1 = 10 KOhm , R2 = 50 KOhm , Rf = 12 KOhm , and V1 = -5V, one can translate and scale the voltage to the desired range.

## Slide 12
A HCS12 member may have one or two 8-channel 10-bit A/D converters.
The highest frequency of the conversion clock is 2 MHz.
At 2 MHz conversion clock, a sample may take 6 ms or 7 ms to complete a conversion
for 8-bit and 10-bit resolution.
An A/D conversion can be started by writing a value to a control register or by an external
trigger input.
The successive approximation method is used to perform the conversion.
The conversion result can be right-justified unsigned, left-justified signed, and
left-justified unsigned.
The HCS12 A/D Converter

## Slide 13
The HCS12 A/D Converter

## Slide 14
Signal Pins Related to A/D Converter
The AD0 module has analog input pins AN0 ~ AN7.
The AD1 module has analog input pins AN8 ~ AN15.
The AN7 pin can be optionally used as the trigger input pin for AD0 module.
The AN15 pin can be optionally used as the trigger input pin for AD1 module.
VRH and VRL are the high and low reference voltage input.
VDDA and VSSA are power supply and ground inputs for the A/D converters.
Registers Related to A/D Converters
Each A/D module has the following registers:
Six control registers: ATDxCTL0 ~ ATDxCTL5. (ATDxCTL0 and ATDxCTL1 are
used for factory testing only).
Two status registers: ATDxSTAT0 and ATDxSTAT1
Two testing registers: ATDxTEST0 and ATDxTEST1
One input enable register: ATDxDIEN
One port data register: PTADx
Eight 16-bit result registers ATDxDR0~ATDxDR7
where, x = 0 or 1
The HCS12 A/D Converter

## Slide 15
ATD Control Register 2 (ATD0CTL2, ATD1CTL2)

## Slide 16
A/D External Triggering
A/D external triggering can be edge-triggering or level-triggering.
The choice of external triggering is controlled by the ATDxCTL2 register.
ATD Control Register 3 (ATD0CTL3 and ATD1CTL3)
This register sets the conversion sequence length, enables/disables the FIFO mode for
result registers, and controls the ATD behavior in freeze mode (BDM mode).
If the FIFO bit is 0, the result of the first conversion appears in the first result register,
the second conversion appears in the second result register, and so on.
If the FIFO bit is 1, then the result of the first conversion appears in the result register
specified by the conversion counter.

## Slide 17
ATD Control Register 3 (ATD0CTL3 and ATD1CTL3)

## Slide 18
This register sets the conversion clock frequency, the length of the second phase of the
sample time, and the resolution of the A/D conversion.
Writes to this register will abort the current conversion.
There are two stages in the sample time. The first stage sample time is fixed at two
conversion clock period. The second stage is selected by SMP1 and SMP0 bits of
this register.
ATD Control Register 4 (ATD0CTL4 and ATD1CTL4)

## Slide 19
ATD Control Register 4 (ATD0CTL4 and ATD1CTL4)

## Slide 20
Selects the type of conversion sequence and the analog input channels to be sampled.
Writes to this register will abort the current conversion.
Table 12.4 selects the channel to be converted.
Table 12.5 summarizes the result data formats available and how they are set up using
the control bits.
Table 12.6 illustrates the difference between the signed and unsigned, left justified
and right justified output codes for an input signal range between 0 and 5.12V.
ATD Control Register 5

## Slide 21
ATD Control Register 5

## Slide 22
ATD Control Register 5

## Slide 23
Each status flag can be cleared by writing a 1 to it.
ATD Status Register (ATD0STAT0 and ATD1STAT0)

## Slide 24
- The SC bit is used to enable special channel conversion.
ATD Test Register 1 (ATD0TEST1, ATD1TEST1)

## Slide 25
A flag can be cleared by one of the following:
(a) Write to ATDxCTL5 register
(b) If AFFC = 0 and read of ATDxSTAT1 followed by read of result register ATDxDRy.
(c) If AFFC = 1 and read of result register ATDxDRy
ATD Status Register 1 (ATD0STAT1, ATD1STAT1)

## Slide 26
This register allows the user to enable a Port ADx pin as a digital input.
Port Data Register (PTAD0, PTAD1)
The port pins are shared with analog inputs AN0~AN7 and AN8~AN15.
ATD Conversion Result Registers (ATDxDRy, x = 0~1, y= 0~7)
Each result register is 16-bit and can be further divided into two 8-bit registers
ATDxDRHy and ATDxDRLy.
The A/D conversion result can be stored right-justified or left-justified.
ATD Input Enable Register (ATD0DIEN, ATD1DIEN)

## Slide 27
The frequency range of the A/D converter clock is from 500 KHz to 2 MHz.
The user sets a prescaler to the bus clock to derive the ATD clock signal.
Sample and Hold Stage
As shown in Figure 12.8, a sample and hold stage accepts analog signals from the input
multiplexer and stores them as charge on the sample capacitor.
The sampling process has two stages.
The first stage of the sampling process takes two A/D clock cycles to charge the
sample capacitor.
The second stage of the sampling process stores the charge in the storage node for a
programmable 2, 4, 8, or 16 cycles.
The conversion time of a sample is given by the following equation:
ATD Module Clock

## Slide 28
The A/D Conversion Time
The A/D conversion time is the sum of the converter time and the sample time.
The conversion timings for 500KHz and 2 MHz are shown in Table 12.8.
Input Channel Wrap Around
In the case of a multiple channel conversion sequence, when input selector goes past
channel AN7, it wraps around to channel AN0.

## Slide 29
Example 1: Assuming that S8C~S1C (ATD0CTL3) are set to 0101 and CC~CA
(ATD0CTL5) are set to 110, what is the conversion sequence for this setting?
Solution:
The first channel to be converted is AN6.
There are five channels to be converted.
The conversion sequence is as follows: AN6, AN7, AN0, AN1, and AN2
FIFO Mode
All eight 16-bit result registers are organized into a circular ring.
The conversion counter in the ATDxSTAT0 register specifies the result register to hold
the current conversion result.
In the FIFO mode, the conversion is not reset to 0 when a new conversion sequence is
started.
In the FIFO mode, the first conversion result may not be stored in ATDxDR0.

## Slide 30
Example 2 Assume that the following setting was programmed before a new
conversion is started:
The conversion counter value in the ATD0STAT0 register is 5.
The channel select code of the ATD0CTL5 register is 6.
The conversion sequence limit of the ATD0CTL3 register is set to 5.
The MULT bit of the ATD0CTL5 register is set to 1.
How would the conversion results be stored when the FIFO mode is selected or not selected?
Solution:
The conversion counter specifies the result register to hold the first conversion result.
The channel select code specifies the first channel to be converted.
The conversion sequence limit specifies the number of channels to be converted.

## Slide 31
Step 1
Connect the hardware properly:
VDDA: connect to VDD (5 V).
VSSA: connect to GND
VRH: connect to VDD (5 V)
VRL: connect to GND
Step 2
If the transducer is not in the appropriate range, use a signal conditioning circuit to shift and
scale it to between VRL and VRH.
Step 3
Select the appropriate channel (s) and operation modes by programming the ATD control
register 5. Writing to the ATDxCTL5 register starts an A/D conversion sequence.
Step 4
Wait until the SCF flag of the status register ATDxSTAT0 is set, then collect the A/D
conversion results and store them in memory.
Procedure for Performing A/D Conversion

## Slide 32
Example 3: Write a subroutine to initialize the AD0 converter for the MC9S12DP256
and start the conversion with the following setting:
nonscan mode
select channel 7 (single channel mode)
fast ATD flag clear all
stop AD0 in wait mode
disable interrupt
perform 4 conversions in a sequence
disable FIFO mode
finish current conversion then freeze when BDM (Background debug mode) becomes active
10-bit operation and 2 A/D clock periods of the second stage sample time
choose 2 MHz as the conversion frequency for the 24 MHz bus clock
result is unsigned and right justified
Solution:
The setting of ATD0CTL2
(a) enable AD0
(b) select fast flag clear all (set bit 6 to 1)
(c) stop AD0 when in wait mode (set bit 5 to 1)
(d) disable external trigger on channel 7 (set bits 4, 3, and 2 to 0)
(e) disable AD0 interrupt (set bit 1 to 0)
Write the value 0xE0 to ATD0CTL2.

## Slide 33
Setting of ATD0CTL3
(a) perform four conversions
(b) disable FIFO mode
(c) when BDM becomes active, complete the current conversion then freeze
Write the value of 0x22 into this control register.
Setting of ATD0CTL4
(a) select 10-bit operation (set bit 7 to 0)
(b) two A/D clock periods for sample time (set bits 6 and 5 to 00)
(c) set the value of PRS4~PRS0 to 00101
Write the value 0x05 to this control register.
Setting of ATD0CTL5
(a) result register right justified (set bit 7 to 1)
(b) result is unsigned (set bit 6 to 0)
(c) nonscan mode (set bit 5 to 0)
(d) single channel mode (set bit 4 to 0)
(e) select channel 7 (set bits 2..0 to 111)
Write the value 0x87 to this control register

## Slide 34
The assembly subroutine that performs the AD0 initialization:
#include "c:\miniide\hcs12.inc"
openATD0 movb #$E0,ATD0CTL2
ldy #2
jsr delayby10us ; wait for 20 us
movb #$22,ATD0CTL3
movb #$05,ATD0CTL4
rts
#include “c:\miniide\delay.asm”
The C function that performs the AD0 initialization:
#include “c:\cwHCS12\include\delay.c”
void openAD0 (void) { ATD0CTL2 = 0xE0;
delayby10us(2); ATD0CTL3 = 0x22; ATD0CTL4 = 0x05; }

## Slide 35
Example 4: Write a program to perform A/D conversion on the analog signal
connected to the AN7 pin. Collect 20 A/D conversion results and store them at memory
locations starting from $1000. Use the same configuration as in Example 3.
Solution:
Example 3 configures AD0 to perform 4 conversions in a sequence on channel AN7.
Need to write into the ATD0CTL5 five times to collect twenty samples.
#include “c:\cwHCS12\include\hcs12.h” void openAD0 (void);
int buf[20]; void main (void) { int i; openAD0(); for (i = 0; i < 5; i++) { ATD0CTL5 = 0x87; // start an A/D conversion while (!(ATD0STAT0 & SCF)); // Has A/D conversion completed? buf[4*i + 0] = ATD0DR0; // save results right justified buf[4*i + 1] = ATD0DR1; buf[4*i + 2] = ATD0DR2; buf[4*i + 3] = ATD0DR3; } asm ("swi");
}

## Slide 36
Liquid Crystal Display (LCD)
The basic construction of an LCD is illustrated in Figure 7.26.
The most common type of LCD allows the light to pass through when activated.
An LCD segment is activated when a low frequency bipolar signal in the range of 30 Hz to 1KHz is applied to it.
LCD can display characters and graphics.
LCDs are often sold in a module with LCDs and controller unit built in.
The Hitachi HD44780 is the most popular character-based LCD controller being used
today.

## Slide 37
A HD44780-Based LCD Kit
- Display capability: 4 x 20
- Uses the HD44780 as the controller as shown in Figure 7.27.
- Pins DB7~DB0 are used to exchange data with the CPU.
- E input should be connected to one of the address decoder output or I/O pin.
- The RS signal selects instruction register (0) or data register (1).
- The VEE signal allows the user to adjust the LCD contrast.
- The HD44780 can be configured to display 1-line, 2-line, and 4-line information.

## Slide 38
Interfacing the HD44780 with the HCS12
One can treat the LCD kit as an I/O device and use an I/O port and several other
I/O pins as control signals.
The interface can be 4 bits or 8 bits. An example of 4-bit interface is shown in Figure 7.28.
To read or write the LCD successfully, one must satisfy the timing requirements of the
LCD.

## Slide 39
Example 5: Write a C program to be run on the Dragon12 (or SSE256) demo board to
display the voltage (output of a potentiometer) connected to the AN7 pin. Configure the
AD0 properly and perform 5 conversions per second and display the voltage on the LCD.
Solution:
The conversion result 1023 corresponds to 5 V.
Need to divide 204.6 into the conversion result to convert the result back to voltage.
Multiply the conversion result by 10 and then divide the product by 2046 to get the voltage.
#include “c:\cwHCS12\include\hcs12.h”
#include “c:\cwHCS12\include\delay.h” // include delay.c in the project
#include “c:\cwHCS12\include\lcd_util.h” // include lcd_util.c in the project
void openAD0(void);
void wait20us (void);
main(void)
{
char buffer[6]; // used to hold the voltage value
int temp;
char *msg1 = "Voltage = ";
openlcd();
buffer[1] = '.'; // decimal point
buffer[3] = 0x20; // space character
buffer[4] = 'V'; // volt character
buffer[5] = 0; // null character

## Slide 40
openAD0();
while(1) {
ATD0CTL5 = 0x87; // convert AN7, result right justified
while(!(ATD0STAT0 & SCF)); // wait for conversion to complete
buffer[0] = 0x30 + (ATD0DR0 * 10 )/2046;
temp = (ATD0DR0 * 10)%2046; // find the remainder
buffer[2] = 0x30 + (temp * 10)/2046; // compute the fractional digit
cmd2lcd(0x80); // set LCD cursor to upper left corner
puts2lcd(msg1); // output the message "voltage ="
puts2lcd(&buffer[0]); // output voltage string
delayby100ms(2); // wait for 200 ms
}
return 0;
}
void openAD0 (void)
{
int i;
ATD0CTL2 = 0xE0; // enable AD0, fast ATD flag clear, disable AD0 in wait mode
delayby10us(2);
ATD0CTL3 = 0x0A; // perform one conversion
ATD0CTL4 = 0x25; // 4 cycles sample time, prescaler set to 12
}
Example 5: Continued.

## Slide 41
Temperature Sensor TC1047A
Has 3 pins with voltage output directly proportional to the ambient temperature.
Can measure temperature in the range of -40oC to 125oC with a supply from 2.7~5.5V.
Voltage output at -40oC, 0oC, 25oC, and 125oC are 100mV, 500mV, 750mV, 1.75V.

## Slide 42
Circuit Connection between the TC1047A and the HCS12
Example 6: Convert the temperature and display it in three integral and one fractional
digits using the LCD. Display the temperature in the whole range of the TC1047A.
Update the display five times a second. E clock is 24 MHz.
Solution:
The whole temperature range is 165oC.
To translate from the A/D conversion result back to temperature, divide the result by
6.2, which can be done by multiplying the result by 10 and then divide the product by 62.

## Slide 43
C program for temperature measurement
#include “c:\cwHCS12\include\hcs12.h”
#include "c:\cwHCS12\include\delay.h" // include delay.c in the project
#include "c:\cwHCS12\include\convert.h“ // include convert.c in the project
#include "c:\cwHCS12\include\lcd_util.h“ // include lcd_util.c in the project
void openAD0(void);
char buf[8];
char *msg1 = "temperature = ";
char *blanks = " ";
void main (void)
{
int temp1,temp2;
char sign,fdigit,frem;
char *ptr;
delayby100ms(2); // wait for LCD kit to initialize
openlcd(); // configure LCD kit
openAD0(); // configure AD0 module
cmd2lcd(0x80); // set cursor to upper left corner
puts2lcd(msg1); // output the message "temperature = "

## Slide 44
while(1) {
sign = 0; // initialize sign to be positive
ATD0CTL5 = 0x87; // start a conversion with result right justified
while(!(ATD0STAT0 & SCF)); // wait until conversion is done
temp1 = (ATD0DR0 * 10) / 62; // integer part of temperature
temp2 = (ATD0DR0 * 10) % 62; // remainder part
temp1 -= 40; // subtract the offset from the actual temperature
if (temp1 < 0){ // temperature is negative
sign = 1;
temp1 = ~temp1 + 1; // find the magnitude of temperature
if (temp2) { // remainder not zero
temp1 --;
temp2 = 62 - temp2;
}
}
fdigit = (temp2 * 10) / 62; // compute the fractional digit
frem = (temp2 * 10)%62;
if (frem > 31) {
fdigit ++;
if (fdigit == 10) { // round off the fraction digit
fdigit = 0;
temp1++;
}

## Slide 45
}
if (sign) {
ptr = &buf[1]; // point to the first space to hold ASCII string
buf[0] = 0x2D; // store minus sign as the first character
}
else
ptr = &buf[0];
int2alpha(temp1,ptr); // convert the integer part to ASCII string
ptr = &buf[0];
while(*ptr) // find the end of the integer string
ptr++;
*ptr++ = '.';
*ptr++ = fdigit + 0x30;
*ptr++ = 223; // add a degree character
*ptr++ = 'C'; // temperature in Celsius
*ptr = 0; // terminate the temperature string
cmd2lcd(0xC0); // move cursor to 2nd row
puts2lcd(blanks); // clear the 2nd row
cmd2lcd(0xC5); // set cursor to column 5 row 2
puts2lcd(&buf[0]); // output the temperature
delayby100ms(2); // wait for 0.2 seconds
}
}

## Slide 46
The Humidity Sensor IH-3606
Provides a linear voltage output from 0.8 to 3.9 V in the full range of relative humidity
0% to 100% with 5 V power supply.
Is light sensitive and should be shielded from light for best result.
Can resist contaminant vapors, such as organic solvents, chlorine, and ammonia.
Requires a 1kHz low-pass filter at its voltage output before it can be converted.

## Slide 47
Circuit Connection between the IH-3605 and the HCS12
The low pass filter is implemented by a 1 KOhm resistor and a 0.16mF capacitor.

## Slide 48
Example 6: Construct a humidity measurement system that consists of the HCS12,
an IH-3605 humidity sensor, and an LCD. The bus clock frequency of the HCS12 is 24 MHz.
Solution:
- To translate from the A/D conversion result back to humidity, divide the conversion
result by 10.23.
- The same operation can be implemented by multiplying the conversion result by 100 and
dividing by 1023.
#include “c:\cwHCS12\include\hcs12.h”
#include “c:\cwHCS12\include\delay.h”
#include “c:\cwHCS12\include\convert.h”
#include “c:\cwHCS12\include\lcd_util_dragon12.h”
void openAD0(void);
char buf[10];
char *msg1 = "humidity = ";
char *blanks = " ";
void main (void)
{
unsigned int quo,rem,frem;
long temp;
char *ptr,fdigit;

## Slide 49
delayby100ms(2); // wait for LCD kit to self initialize
openlcd(); // configure LCD kit
openAD0(); // configure AD0 module
cmd2lcd(0x80); // set cursor to upper left corner
puts2lcd(msg1); // output the message "humidity = "
while(1) {
ATD0CTL5 = 0x87; // start a conversion with result right justified
while(!(ATD0STAT0&SCF)); // wait until conversion is done
temp = (long)ATD0DR0 * 100; // force compiler to use 32-bit to represent
// the product
quo = temp / 1023; // integer part of temperature
rem = temp % 1023; // remainder part
if (quo == 100)
rem = 0; // force highest humidity to 100% only
fdigit = (rem * 10) / 1023; // compute the fractional digit
frem = (rem * 10) % 1023;
if (frem > 511)
fdigit ++;
if (fdigit == 10) { // round off the fraction digit
fdigit = 0;
quo ++;
}

## Slide 50
ptr = &buf[0];
int2alpha(quo,ptr); // convert the integer part to ASCII string
ptr = &buf[0];
while(*ptr) // find the end of the integer string
ptr++;
*ptr++ = '.'; // decimal point
*ptr++ = fdigit + 0x30; // fractional digit
*ptr++ = '%';
*ptr = 0; // terminate the humidity string
cmd2lcd(0xC0); // move cursor to 2nd row
puts2lcd(blanks); // clear the 2nd row
cmd2lcd(0xC5); // set cursor to column 5 row 2
puts2lcd(&buf[0]); // output the humidity
delayby100ms(2); // wait for 0.2 seconds
}
}
void openAD0(void)
{
ATD0CTL2 = 0xE0; // enable AD0, fast ATD flag clear, power-down on wait
ATD0CTL3 = 0x0A; // perform one ATD conversion
ATD0CTL4 = 0x25; // prescaler set to 12, select 4 cycles sample time
delayby10us(2);
}

## Slide 51
Measuring the Barometric Pressure
Barometric pressure is the air pressure existing at any point within earth’s atmosphere.
This pressure can be measured as an absolute pressure (with reference to absolute
vacuum) or can be referenced to some other value or scale.
Absolute pressure is used in meteorology and aviation.
Atmosphere pressure is exponentially related to altitude. Once the pressure at certain
point is measured, the pressure at any other point can be computed.
Barometric pressure can be measured in four different units.

## Slide 52
The SenSym ASCX30AN Pressure Sensor
- Is a 0 to 30 psia (psi absolute) pressure transducer
- The range of barometric pressure is between 28 to 32 inches mercury (in-Hg) or 13.75
to 15.72 psia or 948 to 1083.8 mbar.
- The transducer output is about 0.15V/psi, which would translate to 2.06V to 2.36V.
Pounds per square inch absolute
1 pound = 0.45 kg

## Slide 54
The Circuit Connection between the ASCX30AN and the HCS12
Example 7: Write a program to measure and display the barometric pressure in units
of mbar using the ASCX30AN pressure transducer.
Solution:
- The offset adjustment can be achieved by using a potentiometer.
- The whole barometric pressure range is 135.8 mbar (= 1083.8 – 948).
- To translate back to barometric pressure, divide 7.53 into the A/D conversion result or
multiply the conversion result by 100 and then divide the product by 753 and then
add 948 to the quotient.

## Slide 55
#include “c:\egnu091\include\hcs12.h”
#include “c:\egnu091\include\delay.c”
#include “c:\egnu091\include\convert.c”
#include “c:\egnu091\include\lcd_util_dragon12.c”
void openAD0(void);
char buf[12];
char *msg1 = "pressure = ";
char *blanks = " ";
void main (void)
{
unsigned int quo,rem,frem;
long temp;
char *ptr,fdigit;
delayby100ms(2); /* wait for LCD kit to self initialize */
openlcd(); /* configure LCD kit */
openAD0(); /* configure AD0 module */
cmd2lcd(0x80); /* set cursor to upper left corner */
puts2lcd(msg1); /* output the message "pressure = " */
while(1) {
ATD0CTL5 = 0x87; /* start a conversion with result right justified */
while(!(ATD0STAT0&SCF)); /* wait until conversion is done */

## Slide 56
temp = (long)ATD0DR0 * 100;
quo = temp/753; /* integer part of pressure */
rem = temp%753; /* remainder part */
fdigit = (rem * 10)/753; /* compute the fractional digit */
frem = (rem * 10) % 753;
if (frem > 377)
fdigit ++;
if (fdigit == 10) { /* round off the fractional digit */
fdigit = 0;
quo ++;
}
ptr = &buf[0];
quo = quo + 948;
int2alpha(quo,ptr); /* convert the integer part to ASCII string */
ptr = &buf[0];
while(*ptr) /* find the end of the integer string */
ptr++;
*ptr++ = '.';
*ptr++ = fdigit + 0x30;
*ptr++ = 0x20;
*ptr++ = 'm';

## Slide 57
*ptr++ = 'b';
*ptr++ = 'a';
*ptr++ = 'r';
*ptr = 0; // terminate the barometric pressure string
cmd2lcd(0xC0); // move cursor to 2nd row
puts2lcd(blanks); // clear the 2nd row
cmd2lcd(0xC5); // set cursor to column 5 row 2
puts2lcd(&buf[0]); // output the pressure
delayby100ms(2); // wait for 0.2 seconds
}
}
void openAD0(void)
{
ATD0CTL2 = 0xE0; // enable AD0, fast ATD flag clear, power-down on wait
ATD0CTL3 = 0x0A; // perform one ATD conversion
ATD0CTL4 = 0x25; // prescaler set to 12, select 4 cycles sample time
delayby10us(2);
}

## Slide 58
Digital to Analog Converter (DAC)
A DAC converts fixed-point binary numbers into an electric voltage or current.
The output of a DAC is a linear function of the input.
The input to a DAC is often obtained from a sampling process at uniform intervals.
Applications of DAC include digital gain and offset adjustment, programmable voltage
and current sources, programmable attenuators, digital audio, closed-loop positioning,
robotics, and so on.
Factors to Consider When Choosing a DAC
Resolution
Dynamic range of the output
Number of channels
Type of output

## Slide 59
Digital to Analog Converter (DAC)
The AD7302 D/A Converter
A dual-channel 8-bit D/A converter made by Analog Devices
The AD7302 converts an 8-bit digital value into an analog voltage.
The block diagram is shown in Figure 7.43. The AD7302 is designed to be a memory-
mapped device. The CS signal must be low in order for this chip to work.
The AD7302 needs a reference voltage to operate. The reference voltage could be
external one (from the REFIN pin) or the internal VDD.
Each conversion takes about 2 ms to complete.
The output from either DAC is given by
VOUTA/B = 2 × VREF × (N/256)
where, N is the digital value to be converted.

## Slide 60
Using the AD7302 to generate sawtooth waveform
Configure PB7…PB0, PJ0…PJ1 for output.
Output the digital value from 0 to 255 and repeat. For each value, pull the PJ0 to low and then to high so that the value on pins PB7..PB0 can be transferred to the AD7302.
Pull the signal PJ1 to low during the process.

## Slide 61
Example 8: Write a program to generate a sawtooth waveform from VOUTA pin.
The assembly program is as follows:
#include "c:\miniide\hcs12.inc"
org $1500
start movb #$FF,DDRB ; configure PORTB for output
bset DDRJ,$03 ; configure PJ1~PJ0 for output
bclr PTJ,$02 ; select VOUTA output
loop inc PORTB ; increase the output by one step
bclr PTJ,$01 ; generate a rising edge on PJ0 pin
bset PTJ,$01 ; "
bset PTJ,$01 ; add 9 more “bset” instructions to provide 2 ms
bset PTJ,$01 ; for D/A conversion to complete
bset PTJ,$01 ; "
bset PTJ,$01 ; “
bset PTJ,$01 ; “
bset PTJ,$01 ; "
bset PTJ,$01 ; “
bset PTJ,$01 ; “
bset PTJ,$01 ; “
bra loop ; to complete the D/A conversion
end
The C language version of the program is on next page.

## Slide 62
#include “c:\cwHCS12\include\hcs12.h”
void main(void)
{
DDRB = 0xFF; // configure PORTB for output
DDRJ |= 0x03; // configure pins PJ1~PJ0 for output
PTJ &= 0xFD; // pull the signal A/B to low to select channel A
while (1) {
PORTB += 1;
PTJ &= 0xFE; // generate a rising edge
PTJ |= 0x01; // “
PTJ |= 0x01; // use dummy statements to provide 2 ms
PTJ |= 0x01; // time for D/A conversion to complete
PTJ |= 0x01;
PTJ |= 0x01;
PTJ |= 0x01;
PTJ |= 0x01;
PTJ |= 0x01;
PTJ |= 0x01;
PTJ |= 0x01;
}
}

## Slide 63: Exercises (1)

## Slide 64: Exercises (2)

## Slide 65: Exercises (3)
    The Celsius can be derived from the A/D conversion result using the following equation:
    Celsius temperature = (A/D result) / 8

## Slide 66: Exercises (4)
The Fahrenheit temperature can be derived from the A/D conversion result using the following equation:
Fahrenheit temperature = A/D result / 4

## Slide 67: Exercises (5)
The mass flow in the unit of ml per minute can be computed using the following expression:
mass flow = A/D result x 1000 / 1023

## Slide 68: Content
Basics of A/D Conversion
The HCS12 A/D Converter
Registers Related to A/D Converters
Procedure for Performing A/D Conversion
Temperature Sensor TC1047A
The Humidity Sensor IH-3606
The SenSym ASCX30AN Pressure Sensor
Digital to Analog Converter