## Slide 1: HCS12 Timer Functions
Razvan Bogdan Embedded Systems

## Slide 2: Content
The HCS12 Timer System
Timer Counter Register
Input-Capture Function
Output-Compare Function
Modulus Down Counter
PWM
DC Motor Control

## Slide 3
Why are Timer Functions Important?
The following applications are difficult to implement without a dedicated
timer function:
time delay creation and measurement
period and pulse width measurement
frequency measurement
event counting
arrival time comparison
time-of-day tracking
periodic interrupt generation
waveform generation

## Slide 4
The HCS12 Timer System
The HCS12 has a standard timer module (TIM) that consists of:
Eight channels of multiplexed input capture and output compare functions.
16-bit Pulse Accumulator A
16-bit timer counter
The TIM block diagram is shown in Figure 8.1.
The HCS12 devices in the automotive family have implemented an Enhanced Capture
Timer module (ECT). The ECT module contains:
All the features contained in the TIM module
One 16-bit buffer register for each of the input capture channels.
Four 8-bit pulse accumulator
A 16-bit Modulus Down Counter with 4-bit prescaler
Four user selectable delay counters for increasing input noise immunity
The TIM (of course ECT also) shares the eight Port T pins (IOC0…IOC7).

## Slide 6
Timer Counter Register (TCNT)
Required for input capture and output compare functions.
Must be accessed in one 16-bit operation in order to obtain the correct value.
Three other registers are related to the operation of the TCNT: TSCR1, TSCR2, TFLG2.
Timer System Control Register 1 (TSCR1)
The contents of TSCR1 are shown in Figure 8.2.
Setting and clearing the bit 7 of TSCR1 will start and stop the counting of the TCNT.
Setting the bit 4 will enable fast timer flag clear function. If this bit is clear, then the user must write a one to a timer flag in order to clear it.

## Slide 8
Timer System Control Register 2 (TSCR2)
Bit 7 is the TCNT overflow interrupt enable bit.
TCNT can be reset to 0 when TCNT equals TC7 by setting bit 3 of TSCR2
The clock input to TCNT can be prescaled by a factor selecting by bits 2 to 0 of TSCR2.
The contents of TSCR2 are shown in Figure 8.2.

## Slide 9
Timer Interrupt Flag 2 Register (TFLG2)
Only bit 7 (TOF) is implemented. Bit 7 will be set whenever TCNT overflows.
Input Capture Functions
Physical time is often represented by the contents of the main timer.
The occurrence of an event is represented by a signal edge (rising or falling edge).
The time when an event occurs can be recorded by latching the count of the main timer when a signal edge arrives as illustrated in Figure 8.4.
The HCS12 has eight input capture channels. Each channel has a 16-bit capture register, an input pin, edge-detection logic, and interrupt generation logic.
Input capture channels share most of the circuit with output compare functions. For this
reason, they cannot be enabled simultaneously.
The selection of input capture and output compare is done by programming the TIOS
register.
The contents of the TIOS register are shown in Figure 8.5. Setting a bit select the output compare function. Otherwise, the input capture function is selected.

## Slide 10
The following instruction will enable the output compare channels 7...4 and
input capture channel 3…0:
movb #$F0,TIOS

## Slide 11
Timer Port Pins
Each port pin can be used as a general I/O pin when timer function is not selected.
Pin 7 can be used as input capture 7, output compare 7 action, and pulse
accumulator input.
When a timer port pin is used as a general I/O pin, its direction is configured by
the DDRT register.

## Slide 12
Timer Control Register 3 and 4
The signal edge to be captured is selected by TCTL3 and TCTL4.
The edge to be captured is selected by two bits. The user can choose to capture the rising edge, falling edge, or both edges.

## Slide 13
Timer Interrupt Enable Register (TIE)
The arrival of a signal edge may optionally generate an interrupt to the CPU.
The enabling of the interrupt is controlled by the Timer Interrupt Enable Register.
Timer Interrupt Flag 1 Register (TFLG1)
Whenever a signal edge arrives, the associated timer interrupt flag will be set to 1.

## Slide 14
How to clear a timer flag bit?
In normal mode, write a 1 to the flag bit to be cleared
Method 1. Use the BCLR instruction with a 0 at the bit position (s) corresponding to the
flag (s) to be cleared. For example,
BCLR TFLG1, $FE
will clear the C0F flag.
Method 2. Use the movb instruction with a 1 at the bit position (s) corresponding to the
flag (s) to be cleared. For example,
movb #$01,TFLG1
will clear the C0F flag.
When fast timer flag clear function is enabled, see Figure 8.1.

## Slide 15
Applications of Input Capture Function
Event arrival time recording
Period measurement: need to capture the main timer values corresponding to two
consecutive rising or falling edges
Pulse width measurement: need to capture the rising and falling edges

## Slide 16
Interrupt generation: Each input capture functions can be used as an edge-sensitive
interrupt sources.
Event counting: count the number of signal edges arrived during a period
Time reference: often used in conjunction with an output compare function

## Slide 17
Duty Cycle Measurement
Phase Difference Measurement

## Slide 18
Example 2: Period measurement. Use the input capture channel 0, IC0, to measure the period of an unknown signal. The period is known to be shorter than 128 ms. Assume that the E clock frequency is 24 MHz. Use the number of clock cycles as the unit of the period.
Solution:
Since the input-capture register is 16-bit, the longest period of the signal that can be measured with the prescaler to TCNT set to 1 is:
216 ÷ 24 MHz = 2.73 ms.
To measure a period that is equal to 128 ms, we have two options:
Set the prescale factor to 1 and keep track of the number of times that the timer counter
overflows.
Set the prescale factor to 64 and do not keep track of the number of times that the timer
counter overflows.
We will set the prescale factor to TCNT to 64. The logic flow for measuring the signal
period is shown in Figure 8.16.

## Slide 19
64
C0F -> TFLG1 register 

## Slide 20
Assembly Program for Period Measurement
#include "c:\miniide\hcs12.inc"
org $1000
edge1 ds.b 2 ; memory to hold the first edge
period ds.b 2 ; memory to store the period
org $1500
movb #$90,TSCR1 ; enable timer counter and enable fast timer flags clear
bclr TIOS,IOS0 ; enable input-capture 0
movb #$06,TSCR2 ; disable TCNT overflow interrupt, set prescaler to 64
movb #$01,TCTL4 ; capture the rising edge of PT0 signal
movb #C0F,TFLG1 ; clear the C0F flag
brclr TFLG1,C0F,* ; wait for the arrival of the first rising edge
ldd TC0 ; save the first edge and clear the C0F flag
std edge1
brclr TFLG1,C0F,* ; wait for the arrival of the second edge
ldd TC0
subd edge1 ; compute the period
std period
swi
end

## Slide 21
C Program for Period Measurement
#include "c:\cwHCS12\include\hcs12.h"
void main(void)
{
unsigned int edge1, period;
TSCR1 = 0x90; // enable timer counter, enable fast flag clear
TIOS &= ~IOS0; // enable input-capture 0
TSCR2 = 0x06; // disable TCNT overflow interrupt, set prescaler to 64
TCTL4 = 0x01; // capture the rising edge of the PT0 pin
TFLG1 = C0F; // clear the C0F flag
while (!(TFLG1 & C0F)); // wait for the arrival of the first rising edge
edge1 = TC0; // save the first captured edge and clear C0F flag
while (!(TFLG1 & C0F)); // wait for the arrival of the second rising edge
period = TC0 - edge1;
while(1);
}

## Slide 22
Example 3: Write a program to measure the pulse width of a signal connected to the
PT0 pin. The E clock frequency is 24 MHz.
Solution:
1. Set the prescale factor to TCNT to 32. Use clock cycle as the unit of measurement.
2. The pulse width may be longer than 216 clock cycles, we need to keep track of the number
of times that the TCNT timer overflows. Let
ovcnt = TCNT counter overflow count
diff = the difference of two consecutive edges
edge1 = the captured time of the first edge
edge2 = the captured time of the second edge
The pulse width can be calculated by the following equations:
Case 1
edge2  edge1
pulse width = ovcnt × 216 + diff
Case 2
edge2 < edge 1
pulse width = (ovcnt – 1) × 216 + diff

## Slide 25
#include "c:\miniide\hcs12.inc"
org $1000
edge1 ds.b 2
overflow ds.b 2
PW ds.b 2
org $1500
movw #tov_isr,UserTimerOvf ; set up TCNT overflow interrupt vector
lds #$1500 ; set up stack pointer
movw #0,overflow
movb #$90,TSCR1 ; enable TCNT and fast timer flag clear
movb #$05,TSCR2 ; disable TCNT interrupt, set prescaler to 32
bclr TIOS,IOS0 ; select IC0
movb #$01,TCTL4 ; capture rising edge
movb #C0F,TFLG1 ; clear C0F flag
brclr TFLG1,C0F,* ; wait for the first rising edge
movw TC0,edge1 ; save the first edge & clear the C0F flag
movb #TOF,TFLG2 ; clear TOF flag
bset TSCR2,$80 ; enable TCNT overflow interrupt
cli ; "
movb #$02,TCTL4 ; capture the falling edge on PT0 pin
brclr TFLG1,C0F,* ; wait for the arrival of the falling edge
ldd TC0
subd edge1

## Slide 26
std PW
bcc next ; is the second edge smaller?
ldx overflow ; second edge is smaller, so decrement
dex ; overflow count by 1
stx overflow ; "
next swi
tov_isr movb #TOF,TFLG2 ; clear TOF flag
ldx overflow
inx
stx overflow
rti
end

## Slide 27
C Program for Pulse With Measurement
#include "c:\cwHCS12\include\hcs12.h"
unsigned diff, edge1, overflow;
unsigned long pulse_width;
void main(void)
{
overflow = 0;
TSCR1 = 0x90; // enable timer and fast flag clear
TSCR2 = 0x05; // set prescaler to 32, no timer overflow interrupt
TIOS &= ~IOS0; // select input-capture 0
TCTL4 = 0x01; // prepare to capture the rising edge
TFLG1 = C0F; // clear C0F flag
while(!(TFLG1 & C0F)); // wait for the arrival of the rising edge
TFLG2 = 0x80; // clear TOF flag
TSCR2 |= 0x80; // enable TCNT overflow interrupt
asm("cli");
edge1 = TC0; // save the first edge
TCTL4 = 0x02; // prepare to capture the falling edge
while (!(TFLG1 & C0F)); // wait for the arrival of the falling edge
diff = TC0 - edge1;
if (TC0 < edge1)
overflow -= 1;
pulse_width = (long)overflow * 65536u + (long)diff;
while (1);
}

## Slide 28
interrupt void tovisr(void)
{
TFLG2 = 0x80; // clear the TOF flag
overflow++;
}
The timer overflow vector is set up by using the following function:
extern void near tovisr(void);
#pragma CODE_SEG __NEAR_SEG NON_BANKED
#pragma CODE_SEG DEFAULT // Change code section to DEFAULT.
typedef void (*near tIsrFunc)(void);
const tIsrFunc _vect[] @0xFFDE = {
tovisr
};

## Slide 29
Output Compare Function
The HCS12 has eight output compare channels.
Each output compare channel consists of
1. a 16-bit comparator
2. a 16-bit compare register TCx (also used as input capture register)
3. an output action pin (PTx, can be pulled high, pulled low, or toggled)
4. an interrupt request circuit
5. a forced-compare function (CFOCx)
6. control logic
Operation of the Output-Compare Function
One of the applications of the output-compare function is to trigger an action at a specific time in the future.
To use an output-compare function, the user
1. makes a copy of the current contents of the TCNT register,
2. adds to this copy a value equal to the desired delay, and
3. stores the sum into an output-compare register (TCx, x = 0..7).

## Slide 30
The actions that can be activated on an output compare pin include
1. pull up to high
2. pull down to low
3. toggle
The action is determined by the Timer Control Register 1 & 2 (TCTL1 & TCTL2):

## Slide 31
A successful compare will set the corresponding flag bit in the TFLG1 register.
An interrupt may be optionally requested if the associated interrupt enable bit in the TIE register is set.
Example 4: Generate an active high 1 KHz digital waveform with 30 percent duty cycle from the PT0 pin. Use the polling method to check the success of the output compare operation. The frequency of the E clock is 24 MHz.
Solution:
An active high 1 KHz waveform with 30 percent duty cycle is shown in Figure 8.19. The logic flow of this problem is illustrated in Figure 8.20.
Setting the prescaler to the TCNT to 8, then the period of the clock signal to the TCNT will be 1/3 us. The numbers of clock cycles that the signal is high and low are 900 and 2100, respectively.

## Slide 32
=> We should use interrupt-driven method to generate the waveform so that the CPU can
still perform other operations.

## Slide 33
C Program for Generating 1 KHz Digital Waveform
#include "c:\cwHCS12\include\hcs12.h"
#define HiCnt 900
#define LoCnt 2100
char HiorLo;
void main (void)
{
TSCR1 = 0x90; // enable TCNT and fast timer flag clear
TSCR2 = 0x03; // disable TCNT interrupt, set prescaler to 8
TIOS |= OC5; // enable OC5 function
TCTL1 = 0x0C; // set OC5 action to be pull high
TFLG1 = 0xFF; // clear all CxF flags
TC5 = TCNT + 10;
while(!(TFLG1 & C5F)); // wait until C5F is set
TCTL1 = 0x04; // set OC5 pin action to toggle
TC5 += HiCnt; // start an new OC5 operation
HiorLo = 0; // add LoCnt for the next OC5 operation
TIE = 0x20; // enable OC5 interrupt locally
asm("cli"); // enable interrupt globally
while(1);
}

## Slide 34
interrupt void oc5ISR (void)
{
if(HiorLo){
TC5 += HiCnt;
HiorLo = 0;
}
else {
TC5 += LoCnt;
HiorLo = 1;
}
}
The OC5 interrupt vector is set up using the following function (in vectors.c):
extern void near oc5ISR(void);
#pragma CODE_SEG __NEAR_SEG NON_BANKED
#pragma CODE_SEG DEFAULT // Change code section to DEFAULT.
typedef void (*near tIsrFunc)(void);
const tIsrFunc _vect[] @0xFFE4 = {
oc5ISR
};

## Slide 35
Example 5: Write a function to generate a time delay that is a multiple of 1 ms.
Assume that the E clock frequency is 24 MHz. The number of milliseconds is passed in
Y. Also write an instruction sequence to test this function.
Solution: One method to create 1 ms delay is as follows:
Set the prescaler to TCNT to 8
Perform the number of output-compare operations (given in Y) with each operation
creating a 1-ms time delay.
The number to be added to the copy of TCNT is 3000. (3000  8  24000000 = 1 ms)
delayby1ms pshd
movb #$90,TSCR1 ; enable TCNT & fast flags clear
movb #$03,TSCR2 ; configure prescaler to 8
bset TIOS,OC0 ; enable OC0
ldd TCNT
again0 addd #3000 ; start an output-compare operation
std TC0 ; with 1 ms time delay
wait_lp0 brclr TFLG1,OC0,wait_lp0
ldd TC0
dbne y,again0
puld
rts

## Slide 36
void delayby1ms(int k)
{
int ix;
TSCR1 = 0x90; /* enable TCNT and fast timer flag clear */
TSCR2 = 0x03; /* disable timer interrupt, set prescaler to 8 */
TIOS |= OC0; /* enable OC0 */
TC0 = TCNT + 3000;
for(ix = 0; ix < k; ix++) {
while(!(TFLG1 & C0F));
TC0 += 3000;
}
TIOS &= ~OC0; /* disable OC0 */
}

## Slide 37
Example 6: Generate a sequence of pulses using an OC function. Write a program to generate a number of pulses with the specified high interval duration (12 ms) and low interval duration (8 ms). Use the interrupt-driven approach so that the CPU can perform other operations.
Solution: Let
NN: number of pulses to be generated
DelayHi: high interval duration
DelayLo: low interval duration
HiorLo: flag to select DelayHi or DelayLo
pcnt: number of OC0 operation to be performed
Procedure:
Step 1
Pull the PT0 pin high quickly using the OC0 operation.
Step 2
Change the OC0 pin action to toggle. Start the next OC0 operation with delay equal to DelayHi.
Step 3
pcnt  2 * NN - 1. HiorLo  0.
Step 4
Enable OC0 interrupt.
Step 5
The main program continues to perform other operations.

## Slide 38
#include "c:\cwHCS12\include\hcs12.h"
#include "c:\cwHCS12\include\SetClk.h"
#define DelayHi 18000 // high time of the pulses to be created
#define DelayLo 12000 // low time of the pulses to be created
#define NN 10 // number of pulses to be created
int pcnt; // pulse count
char HiorLo; // flag to choose
void main(void)
{
SetClk8(); // use PLL to generate bus and system clocks
TSCR1 = 0x90; // enable TCNT and faster timer flag clear
TSCR2 = 0x04; // set TCNT clock input prescaler to 16
TFLG1 = C0F; // clear C0F flag
TIOS |= OC0; // enable OC0
TCTL2 = 0x03; // set OC0 pin action to be pull high
TC0 = TCNT + 16; // pull PT0 pin high quickly
while(!(TFLG1 & C0F)); // "
pcnt = 2 * NN - 1;// prepare to create NN pulses (toggle 2 * NN - 1 times)
TCTL2 = 0x01; // set OC0 pin action to be toggle
TC0 += DelayHi; // start the second OC0 operation
HiorLo = 0; // next time use DelayLo as delay count of OC0 operation
TIE |= C0I; // enable TC0 interrupt
asm("cli"); // "
while (1); // do nothing or do something else
}

## Slide 39
interrupt void tc0ISR(void) {
if(HiorLo){
TC0 += DelayHi;
HiorLo = 0;
} else {
TC0 += DelayLo;
HiorLo = 1;
}
pcnt--;
if(pcnt == 0){
TIE = 0; // disable OC0 interrupt
TIOS &= 0xFE; // disable OC0
}
}
The OC0 interrupt vector is set up using the following function (in vectors.c):
extern void near oc0ISR(void);
#pragma CODE_SEG __NEAR_SEG NON_BANKED
#pragma CODE_SEG DEFAULT // Change code section to DEFAULT.
typedef void (*near tIsrFunc)(void);
const tIsrFunc _vect[] @0xFFEE = {
oc0ISR
};

## Slide 40
Using OC7 to Control Multiple OC Functions
OC7 can control up to eight channels of OC functions
The register OC7M specifies which OC channels are controlled by OC7.
The register OC7D specifies the value that any PTx pin to assume when the OC7
operation succeeds.
For OC0 to OC6, when the OC7Mn (n = 0,…,6) bit is set, a successful OC7 compare
overrides a successful OC0…OC6 compare pin action during the same cycle.

## Slide 41
Example 9: What value should be written into OC7M and OC7D if one wants pins
PT2, PT3, and PT4 to assume the values of 1, 0, and 1, respectively when OC7 compare
succeeds?
Solution:
Bits 4, 3, and 2 of OC7M must be set to 1, and bits 4, 3, 2, of OC7D should be set to 1, 0,
and 1, respectively.
The following instruction sequence will achieve the desired effect:
movb #$1C,OC7M
movb #$14,OC7D

## Slide 42
Forced Output-Compare
There are applications in which the user wants an output compare in action to occur
immediately instead of waiting for a match between the TCNT and the proper output
compare register.
This situation arises in the spark plug timing control and some automotive engine
control applications.
To force an output compare operation, write ones to the corresponding bit in the CFORC
register.
At the next timer count after the write to the CFORC register, the forced channels will
trigger their programmed pin actions to occur.

## Slide 43
Example 12: Suppose that the contents of the TCTL1 and TCTL2 registers are $D6 and
$6E, respectively. The contents of the TFLG1 are $00. What would occur on pins PT7 to
PT0 on the next clock cycle if the value $7F is written into the CFORC register?
Solution:
The TCTL1 and TCTL2 configure the output-compare actions as shown in Table8.2.
The TFLG1 register indicates that none of the started output-compare operations
have succeeded yet.
The actions indicated in Table 8.2 will be forced to occur immediately.

## Slide 44
Modulus Down-Counter
Can generate periodic interrupts
Can be used to latch the value of IC registers and the pulse accumulators to their holding
registers.
The action of latching can be periodic or only once.
The clock input (E clock) to the modulus down counter is prescaled by 1, 4, 8, or 16.
The operation of the modulus down counter is controlled by the MCCTL register and the
status of its operation is recorded in the MCFLG register.
The modulus down counter MCCNT is 16-bit.
The MCCNT register has a 16-bit load register, which will be reloaded into MCCNT when
it decrements to 0.
When writing a value into MCCNT, the value is also written into the load register.

## Slide 46
Example 13: Write an instruction sequence to generate periodic interrupt every 10 ms.
Solution: One possible value to be written into the MCCTL register is $C7 which will:
enable MCCNT
enable MCCNT interrupt
enable modulus mode
set prescaler to 16
The instruction sequence to achieve the desired setting is as follows:
movb #$C7,MCCTL
movw #15000,MCCNT ; place the value that will be decremented
; to 0 in 10 ms
cli ; enable interrupt

## Slide 47
Using Modulus Down Counter to generate Time Delay
- It is most convenient to use the non-modulus mode to create time delay.
Example 14: Write a subroutine to create a time delay that is a multiple of 10 ms using
the modulus down counter. The multiple is passed in Y. E clock is 24 MHz.
Solution:
By setting the prescaler to 16, the value of 15000 will take 10 ms to decrement to 0. The
following subroutine will create a time delay equals to a multiple of 10 ms:
delayby10ms
bset TSCR1,TFFCA ; enable timer fast flag clear
movb #$07,MCCTL ; enable modulus down counter with 1:16 as prescaler
movw #15000,MCCNT ; load the value to be down counted
brclr MCFLG,MCZF,*
bclr MCCTL,$04 ; disable modulus down counter
dbne y,delay10ms
rts
Time delays equal to a multiple of 10 ms, 50 ms, 1 ms, 100ms, and 1s can be created by
modifying this subroutine.

## Slide 48
Using Modulus Down Counter to generate Time Delay
- It is most convenient to use the non-modulus mode to create time delay.
Example 14: Write a subroutine to create a time delay that is a multiple of 10 ms using
the modulus down counter. The multiple is passed in Y. E clock is 24 MHz.
Solution:
By setting the prescaler to 16, the value of 15000 will take 10 ms to decrement to 0. The
following subroutine will create a time delay equals to a multiple of 10 ms:
Homework: C delay routines for multiple of 10 ms, 50 ms, 1 ms, 100ms, and 1s 

## Slide 49
Pulse Width Modulation (PWM)
Many applications require the generation of digital waveform.
Output compare function can be used to generate digital waveform but incur too much
overhead.
Pulse width modulation requires only the initial setup of period and duty cycle for
generating the digital waveform.
The MC9S12DP256 has an 8-channel PWM module.
Each PWM channel has a period register, a duty cycle register, a control register, and a
dedicated counter.
The clock input to PWM is programmable through a two-stage circuitry.
There are four possible clock sources for the PWM module: clock A, clock SA, clock B,
and clock SB.
Clock SA is derived by dividing the clock A by an even number ranging from 2 to 512.
Clock SB is derived by dividing the clock B by an even number ranging from 2 to 512.
Clock A and clock B are derived by dividing the E clock by a power of 2. The power
can range from 0 to 7.

## Slide 51
PWM Clock Generation
The prescale factors for clock A and clock B are determined by the PCKA2…PCKA0 and
PCKB2…PCKB0 bits of the PWMPRCLK register.
Clock SA is derived by dividing clock A by the value of the PWMSCLA register and
then dividing by 2.
Clock SB is derived by dividing clock B by the value of the PWMSCLB register and
then dividing by 2.
The clock source selection is controlled by the PWMCLK register.

## Slide 52
PWM Channel Timers
The main part of each PWM channel x consists of an 8-bit counter (PWMCNTx), an
8-bit period register (PWMPERx), and an 8-bit duty cycle register (PWMDTYx).
The waveform output period is controlled by the match between the PWMPERx
register and PWMCNTx register.
The waveform output duty cycle is controlled by the match of the PWMDTYx
register and the PWMCNTx register.
The starting polarity of the output is selectable on a per channel basis by programming
the PWMPOL register.
A PWM channel must be enabled by setting the proper bit of the PWME register.
The overall operation of the PWM module is shown in Figure 8.44.

## Slide 55
PWM Waveform Alignment
PWM output waveform can be left-aligned or center-aligned.
The choice of alignment is controlled by the PWMCAE register.
Left-Aligned Output
The PWMCNTx counter is configured as a count-up counter.
PWMx frequency = Clock(A, B, SA, SB frequency)  PWMPERx
Polarity = 0
PWMx duty cycle = [(PWMPERx – PWMDTYx)  PWMPERx]  100%
Polarity = 1
PWMx duty cycle = [PWMDTYx  PWMPERx]  100%

## Slide 56
Center-Aligned Mode
PWM counter operates as an up/down counter and is set to count up whenever the counter
is equal to $00.
When the counter matches the duty register the output flip-flop changes state, causing the
PWM output to also change state.
A match between the PWM counter and the period register changes the counter direction
from an up-count to a down-count.
When the PWM counter decrements and matches the duty register again, the output
flip-flop changes state causing the PWM output to also change state.
When the PWM counter decrements to 0, the counter direction changes from a down-count
back to an up-count and the period and duty registers are reloaded from their buffers.

## Slide 57
In Center-Aligned Mode,
PWMx frequency = Clock (A, B, SA, or SB) frequency  (2  PWMPERx)
When polarity = 0,
PWMx duty cycle = [(PWMPERx – PWMDTYx)  PWMPERx]  100%
When polarity = 1,
PWMx duty cycle = [PWMDTYx  PWMPERx]  100%

## Slide 58
PWM 16-bit Mode
Two adjacent PWM channels can be concatenated into a 16-bit PWM channel.
The concatenation of PWM channels are controlled by the PWMCTL register.
The 16-bit PWM system is illustrated in Figure 8.49.
When channel k and k+1 are concatenated, channel k is the high-order channel, whereas
channel k+1 is the lower channel. (k is even number). A 16-bit channel outputs from the
lower-order channel pin and is also enabled by the lower-order channel.
Both left-aligned and center-aligned mode apply to the 16-bit mode.

## Slide 60
Example 15: Write an instruction sequence to generate a 100KHz waveform with 50%
duty cycle from the PWM0 pin (PP0). Assume that the E clock frequency is 24 MHz.
Solution: Use the following setting:
select clock A as the clock source to PWM0 and set its prescaler to 2.
select left-aligned mode
load the value 120 into the PWMPER0 register (= 24000000 100000 2)
load the value 60 into the PWMDTY0 register (= 120  50%)
#include “c:\miniide\hcs12.inc”
…
movb #0,PWMCLK ; select clock A as the clock source for PWM0
movb #1,PWMPRCLK ; set clock A prescaler to 2
movb #1,PWMPOL ; channel 0 output high at the start of the period
movb #0,PWMCAE ; select left-aligned mode
movb #$0C,PWMCTL ; 8-bit mode, stop PWM in wait and freeze mode
movb #120,PWMPER0 ; set period value
movb #60,PWMDTY0 ; set duty value
movb #0,PWMCNT0 ; reset the PWM0 counter
bset PWMEN,PWME0 ; enable PWM channel 0

## Slide 61
Example 16: Write an instruction sequence to generate a square wave with 20 ms period
and 60% duty cycle from PWM0 and use center-aligned mode.
Solution:
Select clock A as the clock source and set its prescaler to 2.
Load the value 120 into PWMPER0 register.
PWMPER0 = (20  24,000,000  1000,000)  2  2 = 120
PWMDTY0 = PWMPER0  60% = 72.
movb #0,PWMCLK ; select clock A as the clock source
movb #1,PWMPOL ; set PWM0 output to start with high level
movb #1,PWMPRCLK ; set the PWM0 prescaler to clock A to 2
movb #1,PWMCAE ; select PWM0 center-aligned mode
movb #$0C,PWMCTL ; select 8-bit mode, stop PWM in wait mode
movb #120,PWMPER0 ; set period value
movb #72,PWMDTY0 ; set duty value
bset PWME,PWME0 ; enable PWM channel 0

## Slide 62
Example 16: Write an instruction sequence to generate a square wave with 20 ms period
and 60% duty cycle from PWM0 and use center-aligned mode.
Solution:
Select clock A as the clock source and set its prescaler to 2.
Load the value 120 into PWMPER0 register.
PWMPER0 = (20  24,000,000  1000,000)  2  2 = 120
PWMDTY0 = PWMPER0  60% = 72.

## Slide 63
Example 17: Write an instruction sequence to generate a 50 Hz digital waveform with
80% duty cycle using the 16-bit mode from the PWM1 output pin.
Solution: Using the following setting:
Select clock A as the clock source and set its prescaler to 16
Select left aligned mode and select polarity 1
Load the value 30000 into the PWMPER0:PWMPER1 register.
Load the value 24000 into the PWMDTY0:PWMDTY1 register
movb #0,PWMCLK ; select clock A as the clock source
movb #2,PWMPOL ; set PWM0:PWM1 output to start with high level
movb #4,PWMPRCLK ; set prescaler to 16
movb #$1C,PWMCTL ; concatenate PWM0:PWM1, stop PWM in wait mode
movb #0,PWMCAE ; select left align mode
movw #30000,PWMPER0 ; set period to 30000
movw #24000,PWMDTY0 ; set duty to 24000
bset PWME,PWME1 ; enable PWM0:PWM1

## Slide 64
Example 18: Use PWM to dim the light bulb. Assume that we use the PWM0 output to
control the brightness of a light bulb. Write a C program to dim the light to 10% brightness
gradually in five seconds. The E clock frequency is 24 MHz.
Solution:
Set duty cycle to 100% at the beginning.
Dim the brightness by 10% in the first second and then 20% per second in the following
four seconds.
Load 100 into the PWMPER0 register at the beginning.
Decrement PWMPER0 by 1 every 100 ms during the first second and decrement
PWMPER0 by 2 every 100 ms in the following four seconds.

## Slide 65
void main ()
{
int dim_cnt;
PWMCLK = 0; /* select clock A as the clock source */
PWMPOL = 1; /* make waveform to start with high level */
PWMCTL = 0x0C; /* select 8-bit mode */
PWMPRCLK = 2; /* set clock A prescaler to 4 */
PWMCAE = 0; /* select left-aligned mode */
PWMPER0 = 100; /* set period of PWM0 to 0.1 ms */
PWMDTY0 = 100; /* set duty cycle to 100% */
PWME |= 0x01; /* enable PWM0 channel */
/* reduce duty cycle 1 % per 100 ms in the first second */
for (dim_cnt = 0; dim_cnt < 10 ; dim_cnt ++) {
delayby100ms(1);
PWMDTY0--;
}
/* reduce duty cycle 2% per 100 ms in the next 4 seconds */
for (dim_cnt = 0; dim_cnt < 40; dim_cnt ++) {
delayby100ms(1);
PWMDTY0 -= 2;
}
while (1);
}
#include "c:\cwHCS12\include\hcs12.h"
#include "c:\cwHCS12\include\delay.h"

## Slide 66
DC Motor Control
The DC motor has a permanent magnetic field and its armature is a coil.
When a voltage and a subsequent current flow are applied to the armature, the motor begins to spin.
The voltage level applied across the armature determines the speed of rotation.
Almost every application uses a DC motor requires it reverse its direction of rotation or vary its speed.
Reversing the direction is done by changing the polarity of voltage applied to the motor.
Changing the speed requires varying the voltage level of the input to the motor.
Changing the voltage level can be achieved by varying the pulse width of a digital signal input to the DC motor.
How can I do that?

## Slide 67
DC Motor Control
Ton denotes the on-time and Toff denotes the off time of signal. Period is the sum of both on and off times: Ttotal
Duty cycle is calculated as on-time to the period of time
PWM signal when used at a different duty cycles gives a varying voltage at the output
Voltage regulation is done by averaging the PWM signal
As you can see from the equation the output voltage can be directly varied by varying the Ton value.
If Ton is 0, Vout is also 0. if Ton is Ttotal then Vout is Vin or say maximum

## Slide 68
DC Motor Control
The HCS12 can interface with a DC motor through a driver as shown in Figure 8.52.
A suitable driver must be selected to take control signals from the HCS12 and deliver the necessary voltage and current to the motor.
An example of DC motor driver is shown in Figure 8.53.
The L293 has two supply voltages: VSS and VS. VSS is logic supply and can be from 4.5 to 36V. VS is analog and can be as high as 36 V.
Pin 2
Pin 7

## Slide 69
DC Motor Control

## Slide 70
DC Motor Control
As you can see in the figure above there are four switching elements named as "High side left", "High side right", "Low side right", "Low side left". When these switches are turned on in pairs motor changes its direction accordingly. Like, if we switch on High side left and Low side right then motor rotate in forward direction, as current flows from Power supply through the motor coil goes to ground via switch low side right.

## Slide 71
DC Motor Control
Homework: Write a program that controls the direction of DC motor, without taking into consideration any feedback from the motor. Also build a function that stops or decelerates the dc motor. Use the above table and the connections from the figure.
HCS12 PP7
HCS12 PP3

## Slide 72
DC Motor Feedback
The DC motor speed must be fed back to the microcontroller so that it can be controlled.
The motor speed can be fed back by using an optical encoder, infrared detector, or a Hall-effect sensor.
Basing on the speed feedback, the microcontroller can make adjustment to increase or decrease the speed, reverse the direction, or stop the motor.
Assuming two magnets are attached to the shaft (rotor) of a DC motor and a Hall-effect transistor is mounted on the armature (stator).
As shown in Figure 8.54, every time the Hall-effect transistor passes through the magnetic field, it generates a pulse.
The input capture function of the HCS12 can capture the passing time of the pulse. The time between two captures is half of a revolution. Thus the motor speed can be calculated.
Pin 2
Pin 7

## Slide 74
A HCS12-based DC Motor Control System
Schematic is shown in 8.55.
The PWM output from the PP3 pin is connected to one end of the motor whereas the PP7 pin is connected to the other end of the motor.
The circuit is connected so that the motor will rotate clockwise when the voltage of the PP7 pin is 0 while the PWM output is nonzero (positive).
The direction of motor rotation is illustrated in Figure 8.56.
By applying appropriate voltages on PP7 and PP3 (PWM3), the motor can rotate clockwise, counterclockwise, or even stop.

## Slide 75
A HCS12-based DC Motor Control System
Input capture channel 0 is used to capture the feedback from the Hall-effect transistor.
When a DC motor is first powered, it takes time for the motor to reach its final speed.
When a load is added to the motor, it will be slowed down and hence the duty cycle of the PWM3 should be increased to keep the speed constant.
When the load is reduced, the speed of the motor will be increased and hence the duty cycle of the PWM3 should be decreased.
A DC motor does not respond to the change of the duty cycle instantaneously. Several cycles must be allowed for the microcontroller to determine if the change of the duty
cycle has achieved its effect.

## Slide 77
Example 19: Write a subroutine in C language to measure the motor speed (in rpm) assuming E clock is 16 MHz.
Solution:
- Two consecutive rising edges on the PT0 pin must be captured in order to measure the motor speed.
- Let diff be the difference of two captured edges and the period is set to 1 ms, then
Speed = 60 × 106 ÷ (2 × diff)

## Slide 78
#include “c:\cwHCS12\include\hcs12.h”
unsigned int motor_speed (void) { unsigned int edge1, diff, rpm; long int temp; TSCR1 = 0x90; /* enable TCNT and fast flag clear */ TIOS &= IOS0; /* select IC0 function */ TSCR2 = 4; /* set TCNT prescale factor to 16 */
TCTL4 = 0x01; /* select to capture the rising edge of PT0 */ TFLG1 = C0F; /* cleared C0F flag */ while (!(TFLG1 & C0F)); /* wait for the first edge */ edge1 = TC0; while (!(TFLG1 & C0F)); /* wait for the second edge */ diff = TC0 - edge1; temp = 1000000 / (long)(2 * diff); rpm = temp * 60; return rpm; }

## Slide 79
Electrical Braking
Electrical braking is done by reversing the voltage applied to the motor for appropriate amount of time.
In Figure 8.56, the motor can be braked by
reducing the PWM duty-count to 0,
setting the PP7 pin output to high for an appropriate amount of time.

## Slide 80: Content
The HCS12 Timer System
Timer Counter Register
Input-Capture Function
Output-Compare Function
Modulus Down Counter
PWM
DC Motor Control

## Slide 81
Homework:
1. C delay routines for multiple of 10 ms, 50 ms, 1 ms, 100ms, and 1s

## Slide 82
Homework: Write a program that controls the direction of DC motor, without taking into consideration any feedback from the motor. Also build a function that stops or decelerates the dc motor. Use the above table and the connections from the figure.
HCS12 PP7
HCS12 PP3