## Slide 1: Serial Peripheral Interface
Razvan Bogdan Embedded Systems

## Slide 2: Content
What is Serial Peripheral Interface (SPI)?
The HCS12 SPI Modules
SPI Related Registers
The I2C Protocol
An Overview of the HCS12 I2C Module

## Slide 3
What is Serial Peripheral Interface (SPI)?
SPI is a synchronous serial protocol proposed by Motorola to be used as a standard for
interfacing peripheral chips to a microcontroller.
Devices operate in master or slave mode.
The SPI protocol uses four wires to carry out the task of data communication:
MOSI: master out slave in
MISO: master in slave out
SCK: serial clock
SS: slave select
An SPI data transfer is initiated by the master device. A master is responsible for
generating the SCK signal to synchronize the data transfer.
The SPI protocol is mainly used to interface with shift registers, LED/LCD drivers, phase
locked loop chips, memory components with SPI interface, or A/D or D/A converter
chips.

## Slide 4
The HCS12 SPI Modules
An HCS12 device may have from one to three SPI modules.
The MC9S12DP256 has three SPI modules: SPI0, SPI1, and SPI2.
By default, the SPI0 share the use of the upper 4 Port S pins:
PS7  SS0 (can be rerouted to PM3)
PS6  SCK0 (can be rerouted to PM5)
PS5  MOSI0 (can be rerouted to PM4)
PS4  MISO0 (can be rerouted to PM2)
By default, the SPI1 shares the use of the lower 4 Port P pins:
PP3  SS1 (can be rerouted to PH3)
PP2  SCK1 (can be rerouted to PH2)
PP1  MOSI1 (can be rerouted to PH1)
PP0  MISO1 (can be rerouted to PH0)
By default, the SPI2 shares the use of the upper 4 Port P pins:
PP6  SS2 (can be rerouted to PH7)
PP7  SCK2 (can be rerouted to PH6)
PP5  MOSI2 (can be rerouted to PH5)
PP4  MISO2 (can be rerouted to PH4)
It is important to make sure that there is no conflict in the use of signal pins when making rerouting decision.

## Slide 5
SPI Related Registers
The operating parameters of each SPI module are controlled by two control registers:
SPIxCR1: (x = 0, 1, or 2)
SPIxCR2
The baud rate of the SPI transfer is controlled by the SPIxBR register
The operation status of the SPI operation is recorded in the SPIxSR register.
The contents of the SPIxCR1, SPIxCR2, SPIxBR, and SPIxSR registers are illustrated
in Figure 10.1 to 10.4, respectively.
The SS pin may be disconnected from SPI by clearing the SSOE bit in the SPIxCR1
register. After that, it can be used as a general I/O pin.
If the SSOE bit in the SPIxCR1 register is set to 1, then the SS signal will be asserted
to enable the slave device whenever a new SPI transfer is started.
The equation for setting the SPI baud rate is given in Figure 10.3.
The term baud rate is defined as the number of signal changes per second

## Slide 9
Example 1: Give a value to be loaded to the SPIxBR register to set the baud rate to 2 MHz for a 24 MHz bus clock.
Solution: 24 MHz  2 MHz = 12. One possibility is to set SPPR2-SPPR0 and SPR2-SPR0
to 010 and 001, respectively. The value to be loaded into the SPIxBR register is $21.
Example 2: What is the highest possible baud rate for the SPI with 24 MHz bus clock?
Solution: The highest SPI baud rate occurs when both the SPPR2-SPPR0 and SPR2-SPR0
are 000. In this case the baud rate is 24 MHz  2 = 12 MHz.
SPI Transmission Format
The data bits can be shifted on the rising or the falling edge of the SCK clock.
Since the SCK can be idle high or idle low, there are four possible combinations as
shown in Figure 10.5 and 10.6.
To shift data bits on the rising edge, set CPOL-CPHA to 00 or 11.
To shift data bits on the falling edge, set CPOL-CPHA to 01 or 10.
Data byte can be shifted in and out most significant bit first or least significant bit first.

## Slide 12
Bidirectional Mode (MOMI or SISO)
A mode that uses only one data pin to shift data in and out.
This mode is provided to deal with peripheral devices with only one data pin.
Either the MOSI pin or the MISO pin can be used as the bidirectional pin.
When the SPI is configured to the master mode (MSTR bit = 1), the MOSI pin is used in data transmission and becomes the MOMI pin.
When the SPI is configured to the slave mode (MSTR bit = 0), the MISO pin is used in data transmission and becomes the SISO pin.
The direction of each serial pin depends on the BIDIROE bit of the SPIxCR2 register.
The pin configuration for MOSI and MISO are illustrated in Figure 10.7.
If one wants to read data from the peripheral device, clear the BIDIROE bit to 0.
If one wants to output data to the peripheral device, set the BIDIROE bit to 1.

## Slide 14
Mode Fault Error
If the SSx signal goes low while the SPIx is configured as a master, it indicates a
system error where more than one master may be trying to drive the MOSIx and SCKx
pins simultaneously.
The MODF bit in the SPIxSR register will be set to 1 when mode fault condition occurs.
When mode fault occurs, the MSTR bit will be cleared to 0 and the output enable for
the MOSIx and SCKx pins will be deasserted.
SPI Circuit Connection
In an SPI system, one device is configured as a master. Other devices are configured as
slaves.
The circuit connection for a single-slave system is shown in Figure 10.8.
A multi-slave system may have two different connection methods as illustrated in
Figure 10.9 and 10.10.
In Figure 10.9, the master can exchange data with each individual slave without affecting
other slaves.
In Figure 10.10, all the slaves are configured into a larger ring. A data transmission
with certain slave will go through other slaves.

## Slide 17
Solution: fE / baud rate = 24 MHz/6 MHz = 4. We need to set SPPR2-SPPR0 and
SPR2-SPR0 to 001 and 000, respectively. Write the value $10 into the SPI0BR register.
The following instruction sequence will configure the SPI0 as desired:
movb #$10,SPI0BR ; set baud rate to 6 MHz
movb #$50,SPI0CR1 ; disable interrupt, enable SPI, SCK idle low, data ; latched on rising edge, data transferred msb first
movb #$02,SPI0CR2 ; disable bidirectional mode, stop SPI in wait mode
movb #0,WOMS ; enable Port S pull-up
Example 3: Configure the SPI0 to operate with the following setting assuming that
E clock is 24 MHz:
6 MHz baud rate
enable SPI0 to master mode
SCK0 pin idle low with data shifted on the rising edge of SCK
transfer data most significant bit first and disable interrupt
disable SS0 function
stop SPI in Wait mode.
normal SPI operation (not bidirectional mode)
Homework: Write the C variant for Example 3 

## Slide 18
SPI Utility Functions
The following operations are common in many applications and should be made into
library functions to be called by many SPI applications:
(a) Send a character to SPI  putcspix (x = 0, 1, or 2)
(b) Send a string to SPI  putsspix (x = 0, 1, or 2)
(c) Read a character from SPI  getcspix (x = 0, 1, or 2)
(d) Read a string from SPI  getsspix (x = 0, 1, or 2)
Function putcSPI0
putcspi0 brclr SPI0SR,SPTEF,* ; wait until write operation is permissible
staa SPI0DR ; output the character to SPI0
brclr SPI0SR,SPIF,* ; wait until the byte is shifted out
ldaa SPI0DR ; clear the SPIF flag
rts
void putcspi0 (char cx)
{
char temp;
while(!(SPI0SR & SPTEF)); // wait until write is permissible
SPI0DR = cx; // output the byte to the SPI
while(!(SPI0SR & SPIF)); // wait until write operation is complete
temp = SPI0DR; // clear the SPIF flag
}

## Slide 19
Function putsSPI0
; the string to be output is pointed to by X
putsspi0 ldaa 1,x+ ; get one byte to be output to SPI port
beq doneps0 ; reach the end of the string?
jsr putcspi0 ; call subroutine to output the byte
bra putsspi0 ; continue to output
doneps0 rts
void putsspi0(char *ptr)
{
while(*ptr) { /* continue until all characters have been output */
putcspi0(*ptr);
ptr++;
}
}

## Slide 20
Function getcSPI0
; This function reads a character from SPI0 and returns it in accumulator A
getcspi0 brclr SPI0SR,SPTEF,* ; wait until write operation is permissible
staa SPI0DR ; trigger eight clock pulses for SPI transfer
brclr SPI0SR,SPIF,* ; wait until a byte has been shifted in
ldaa SPI0DR ; return the byte in A and clear the SPIF flag
rts
char getcspi0(void)
{
while(!(SPI0SR & SPTEF)); // wait until write is permissible
SPI0DR = 0x00; // trigger 8 SCK pulses to shift in data
while(!(SPI0SR & SPIF)); // wait until a byte has been shifted in
return SPI0DR; // return the character
}

## Slide 21
; This function reads a string from the SPI and store it in a buffer pointed to by X
; The number of bytes to be read in passed in accumulator B
getsspi0 tstb ; check the byte count
beq donegs0 ; return when byte count is zero
jsr getcspi0 ; call subroutine to read a byte
staa 1,x+ ; save the returned byte in the buffer
decb ; decrement the byte count
bra getsspi0
donegs0 clr 0,x ; terminate the string with a NULL character
rts
Function getsSPI0
void getsspi0(char *ptr, char count)
{
while(count) { // continue while byte count is nonzero
*ptr++ = getcspi0(); // get a byte and save it in buffer
count--;
}
*ptr = 0; // terminate the string with a NULL
}

## Slide 22
The HC595 Shift Register
The HC595 consists of an 8-bit shift register and a D-type latch with three-state parallel output.
The shift register provides parallel data to the latch.
The maximum data shift rate is 100 MHz (Philips part).

## Slide 23
Signal Pins of the HC595
- DS: serial data input
- SC: shift clock. A low-to-high transition on this pin causes the data at the serial input pin to be shifted into the 8-bit shift register.
- Reset. A low on this pin resets the shift register portion of this device.
- LC: latch clock. A low-to-high transition on this pin loads the contents of the shift register into the output latch.
- OE: output enable. A low on this pin allows the data from the latches to be presented at the outputs.
- QA to QH: tri-state latch output
- SQH: the output of the eight stage of the shift register
Applications of the HC595
The HC595 is often used to add parallel ports to the microcontroller.
Both the connection methods shown in Figure 10.9 and 10.10 can be used to add parallel ports to the MCU.

## Slide 24
Example 5: Describe how to use two 74HC595s to drive eight common cathode seven
segment displays assuming that the E clock frequency of the HCS12 is 24 MHz.
Solution:
Two 74HC595s can be cascaded using the method shown in Figure 10.10. One
74HC595 is used to hold the seven-segment pattern, whereas the other 74HC595 is used to carry digit-select signals. The circuit connection is shown in Figure 10.12.
Since there are only seven segments, the QH bit of the segment-control 74HC595 is not
needed. The PK7 pin is used to control the LC input of the 74HC595. The time-multiplexing
technique illustrated in connecting the 7seg will be used to display multiple digits in
Figure 10.12
To light the digit on display 7, the voltage at QH of the digit-select 74HC595 must be driven to high. To light the digit on display 6, the voltage at QG of the digit-select 74HC595 must be driven to high, and so on.

## Slide 25
Example 5: Describe how to use two 74HC595s to drive eight common cathode seven
segment displays assuming that the E clock frequency of the HCS12 is 24 MHz.
Solution:

## Slide 26
Example 5: Describe how to use two 74HC595s to drive eight common cathode seven
segment displays assuming that the E clock frequency of the HCS12 is 24 MHz.
Solution: Use the circuit in figure 10.12 to connect two 74HC595s to the HCS12.

## Slide 27
Program to display 87654321 on display #7 to #0.
#include “c:\miniide\hcs12.inc"
org $1000
icnt ds.b 1 ; loop count
org $1500
lds #$1500 ; set up stack pointer
bset DDRK,$80 ; configure the PK7 pin for output
jsr openspi0 ; configure SPI0
forever ldx #dispTab ; use X as a pointer to the table
movb #8,icnt ; set loop count to 8
loop ldaa 1,x+ ; send the digit select byte to the 74HC595
jsr putcspi0 ; "
ldaa 1,x+ ; send segment pattern to 74HC595
jsr putcspi0 ; "
bclr PTK,BIT7 ; transfer data from shift register to output
bset PTK,BIT7 ; latch
ldy #1 ; display the digit for one ms
jsr delayby1ms ; "
dec icnt ;
bne loop ; if not reach digit 1, then next
bra forever ; start from the start of the table

## Slide 28
openspi0 movb #0,SPI0BR ; set baud rate to 12 MHz
movb #$50,SPI0CR1 ; disable interrupt, enable SPI, SCK idle low,
; latch data on rising edge, transfer data msb first
movb #$02,SPI0CR2 ; disable bidirectional mode, stop SPI in wait mode
movb #0,WOMS ; enable Port S pull-up
rts
#include "c:\miniide\delay.asm"
#include "c:\miniide\spi0util.asm"
; ********************************************************************
; Each digit consists of two bytes of data. The first byte is
; digit select, the second byte is the digit pattern.
; ********************************************************************
dispTab dc.b $80,$7F,$40,$70,$20,$5F,$10,$5B
dc.b $08,$33,$04,$79,$02,$6D,$01,$30
end

## Slide 29
#include "c:\cwHCS12\include\hcs12.h"
#include "c:\cwHCS12\include\spi0util.h" // include spi0util.c into the project
#include "c:\cwHCS12\include\delay.h" // include delay.c into the project
void openspi0(void);
void main (void)
{
unsigned char disp_tab[8][2] = {{0x80,0x7F},{0x40,0x70},{0x20,0x5F},{0x10,0x5B},
{0x08,0x33},{0x04,0x79},{0x02,0x6D},{0x01,0x30}};
char i;
openspi0(); /* configure the SPI0 module */
DDRK |= BIT7; /* configure pin PK7 as output */
while(1) {
for (i = 0; i < 8; i++) {
putcspi0(disp_tab[i][0]); /* send out digit select value */
putcspi0(disp_tab[i][1]); /* send out segment pattern */
PTK &= ~BIT7; /* transfer values to latches of 74HC595s */
PTK |= BIT7; /* " */
delayby1ms(1); /* display a digit for 1 ms */
}
}
}

## Slide 30
The TC72 Digital Thermometer
Ten-bit resolution and SPI interface
Pin assignment and block diagram shown in Figure 10.13.
Capable of reading temperature from -55oC to 125oC.
Can be used in continuous temperature conversion or one-shot conversion mode.
Has internal clock generator to control the automatic temperature conversion sequence.

## Slide 31
Temperature Data Format
Temperature is represented by a 10-bit two’s complement word with a resolution of
0.25oC per least significant bit.
The converter is scaled from -128oC to +127oC with 0oC represented as 0x0000.
The temperature value is stored in two 8-bit registers.
Whenever the most significant bit is 1, the temperature is negative.
A sample of temperature reading is shown in Table 10.3.

## Slide 32
TC72’s Serial Interface
The CE input to the TC72 must be asserted (high) to enable SPI transfer.
Data can be shifted on the rising edge or the falling edge depending on the idle polarity
of the SCK source.
Data transfer to and from the TC72 consists of one address byte followed by one or
multiple data (2 to 4) bytes.
The TC72 registers and their addresses are shown in Table 10.4.
The most significant bit of the address byte determines whether a read (A7 = 0) or a
write (A7 = 1) operation will occur.
A multiple byte read operation will start from high address toward lower addresses.
The user can send in the temperature result high byte address and read the temperature
result high byte, low byte, and the control registers.

## Slide 33
Procedure for reading the temperature
Step 1
Pull the CE pin high to enable SPI transfer.
Step 1
Send the temperature result high byte read address (0x02) to the TC72. Wait until the SPI
transfer complete.
Step 3
Read the temperature result high byte. The user needs to write a dummy byte into the SPI
data register to trigger eight clock pulses.
Step 4
Read the temperature result low byte. Again the user needs to write a dummy byte into the
SPI data register to trigger eight clock pulses.
Step 5
Pull CE pin to low so that a new transfer can be started.

## Slide 34
Control Register
The control register is used to select the shutdown, continuous, or one-shot conversion
operating mode.
The temperature conversion mode selection logic is shown in Table 10.5.
At power up, the SHDN bit is 1. Thus the TC72 is in the shutdown mode.
If the SHDN bit is 0, the TC72 will perform a temperature conversion approximately
every 150 ms.
A temperature conversion will be initiated by a write operation into the control register
to select the continuous mode or one-shot mode.
A typical circuit connection between the TC72 and the HCS12 is shown in Figure 10.16.

## Slide 35
Example 6: Write a C program to read the temperature every 200 ms. Convert the
temperature to a string so that it can be displayed in an appropriate output device.
A pointer to hold the string will be passed to this function. The bus clock is 24 MHz.

## Slide 36
#include "c:\cwHCS12\include\hcs12.h"
#include "c:\cwHCS12\include\spi0util.h“ // need to include delay.c, spi0Util.c and
#include "c:\cwHCS12\include\delay.h“ // convert.c into the project
void read_temp (char *ptr);
void openspi0(void);
char buf[10];
void main (void)
{
DDRM |= BIT1; // configure the PM1 pin for output
openspi0(); // configure SPI0 module
read_temp(&buf[0]);
}
void openspi0(void)
{
SPI0BR = 0x10; // set baud rate to 6 MHz
SPI0CR1 = 0x50; // enable SPI0 to master mode, select rising edge to
// shift data in and out
SPI0CR2 = 0x02; // select normal mode and stop SPI in wait mode
WOMS = 0x00; // enable Port S pull-up
}

## Slide 37
void int2alpha(unsigned int xx, char *ptr) {
int quo;
*(ptr+2) = xx % 10 + 0x30; // derive ASCII code of the one’s digit
quo = xx / 10;
if(quo != 0){
*(ptr+1) = quo % 10 + 0x30; // derive the ASCII code of ten’s digit
quo = quo / 10; // hundred’s digit
}
if(quo != 0)
*ptr = quo + 0x30; // derive the ASCII code of hundred’s digit
}

## Slide 38
void read_temp (char *ptr)
{
char hi_byte, lo_byte, temp, *bptr;
unsigned int result;
bptr = ptr;
PTM |= BIT1; /* enable TC72 data transfer */
putcspi0(0x80); /* send out TC72 control register write address */
putcspi0(0x11); /* perform one shot conversion */
PTM &= ~BIT1; /* disable TC72 data transfer */
delayby100ms(2); /* wait until temperature conversion is complete */
PTM |= BIT1; /* enable TC72 data transfer */
putcspi0(0x02); /* send MSB temperature read address */
hi_byte = getcspi0(); /* read the temperature high byte */
lo_byte = getcspi0(); /* save temperature low byte and clear SPIF */
PTM &= ~BIT1; /* disable TC72 data transfer */
lo_byte &= 0xC0; /* make sure the lower 6 bits are 0s */
result = (int) hi_byte * 256 + (int) lo_byte;
if (hi_byte & 0x80) { /* temperature is negative */
result = ~result + 1; /* take the two' complement of result */
result >>= 6;

## Slide 39
temp = result & 0x0003; // place the lowest two bits in temp
result >>= 2; // get rid of fractional part
*ptr++ = 0x2D; // store the minus sign
int2alpha(result, ptr);
}
else { // temperature is positive
result >>= 6;
temp = result & 0x0003; // save fractional part
result >>= 2; // get rid of fractional part
int2alpha(result, ptr); // convert to ASCII string
}
while(*bptr){ // search the end of the string
bptr++;
};
switch (temp){ // add fractional digits to the temperature
case 0:
break;
case 1: // fractional part is .25
*bptr++ = 0x2E; // add decimal point
*bptr++ = 0x32;
*bptr++ = 0x35;
*bptr = '\0';
break;

## Slide 40
case 2: /* fractional part is .5 */
*bptr++ = 0x2E; /* add decimal point */
*bptr++ = 0x35;
*bptr = '\0';
break;
case 3: /* fractional part is .75 */
*bptr++ = 0x2E; /* add decimal point */
*bptr++ = 0x37;
*bptr++ = 0x35;
*bptr = '\0';
break;
default:
break;
}
}

## Slide 41
Homework: Write the C variant for Example 3 

## Slide 43
Inter-Integrated Circuit (I2C) Interface

## Slide 44
The I2C Protocol
Developed by Philips in late 1980s
Version 1.0 was published in 1992. This version supports standard (100 Kbps) and fast
(400 Kbps) mode.
Version 2.0 was published in 1998. The high-speed mode (3.4 Mbps) was added.
Classifies devices into slave and master
Allow multiple masters to be attached to the same bus
The master device uses either a 7-bit or 10-bit address to specify the slave device as its
partner of data communication.
Supports bi-directional data transfer
Allow multiple masters (microcontrollers) to share the same peripheral devices
I2C Signal Level
Float high and driven low
Use the SCL signal to carry clock signal to synchronize data transfer
Use the SDA signal to carry data and address
The SDA and SCL pins of I2C devices (masters and slaves) are open-drain and need
external pull up resistors
The resistors 2.2 KW and 1 KW are recommended for 100 kbps and 400 kbps baud rate.

## Slide 46
Signal Components
I2C data transfer consists of 5 signal components:
(a) Start (S)
(b) Stop (P)
(c) Repeated Start (R)
(d) Data
(e) Acknowledge (A)
Start Condition
Used to indicate that a device would like to transfer data on the I2C bus
Represented by the SDA line going low when the clock (SCL) signal is high
Will initialize the I2C bus

## Slide 47
Stop Condition
A condition that a device wants to release the I2C bus
Is represented by the SDA signal going high when the SCL signal is high
Once the stop condition is complete, both the SCL and SDA signals are high. This is
the idle bus.

## Slide 48
Repeated Start (R) Condition
A Start signal generated without first generating a Stop condition to terminate the
communication
Used by the master to communicate with another slave or change data transfer direction
without releasing the bus
Also referred to as Restart condition

## Slide 49
Data
Represents the transfer of eight bits of information
Data on the SDA line is considered valid only when the SCL signal is high.
When the SCL signal is low, data is allowed to change.
The eight-bit data may be a control code, an address, or data.

## Slide 50
Acknowledge (ACK) Condition
Data transfer needs to be acknowledged either positively (A) or negatively (NACK).
A device acknowledges a byte it received positively by bringing the SDA line low
during the ninth clock pulse of SCL.
If the device allows the SDA line to float high, it is transmitting a negative
acknowledge (NACK).

## Slide 51
Synchronization
All masters generate their clocks on the SCL line to transfer messages on the I2C bus.
A defined clock is needed for the bit-by-bit arbitration procedure to take place.
Most microcontrollers generate the SCL clock by counting down a programmable
reload value using the instruction clock signal.
Clock synchronization occurs when multiple masters attempt to drive the I2C bus and
before the arbitration scheme can decide which master is the winner.
Clock synchronization is performed using the wired-AND connection of I2C interfaces
to the SCL line.
The high-to-low transition on the SCL line causes the devices concerned (masters) to
start counting off their low period.
A master device that is counting off their low period will hold the SCL line low until
the counter is count down to 0. At this point the device will release the SCL line to high.
If there is other devices holding the SCL low, then the SCL line will remain low until all
master devices have counted down to 0. At this point, the SCL line will go high and
all devices will start to count high.
The SCL line will be held low by the device with the longest low period.
By the same reasoning, the high period of the SCL signal is determined by the device
with the shortest high period.

## Slide 52
Handshaking
The clock synchronization mechanism can be used as a handshake in data transfer.
Slave device can hold the SCL line low after completion of one byte transfer (9 bits).
Slave halts the bus until it gets ready for the next operation and then release the
SCL line.

## Slide 53
Arbitration
In the event two or more master devices attempt to begin a transfer at the same time, an arbitration scheme is employed to force one or more masters to give up the bus.
The master devices continue to transmit data until one master attempt to send a high while the other transmits a low.
Since the SDA bus has open drain, the master device that attempts to send a high will detect a low. At this point, it will stop driving the bus.
The arbitration process does not slow down the winning master’s transfer and no data gets lost.

## Slide 54
I2C Addressing Methods
I2C protocol allows master devices to use either the 7-bit and 10-bit address to specify the
slave device for data communication.
The 7-bit addressing uses the upper 7 bits of the address byte for address and the least
significant bit to specify the data transfer direction. The format is shown in Figure 11.13.
The 10-bit addressing uses two bytes to carry the address information.
(a) The bit 0 of the high byte is used to indicate the data transfer direction.
(b) The upper 7 bits have the pattern of 1111 0xx with xx representing the most
significant two address bits of the slave.
(c) The second byte carries the lower 8 address bits.

## Slide 55
Data Transfer Format (7-bit addressing)
Master transmitter to slave receiver – shown in Figure 11.10.
Master reads slave immediately after the first byte (address byte) – shown in Figure
11.11.
Combined format. A master may transfer some data to the slave and then generate a
restart condition to read data from the slave or send/read data to/from other slave.
-- shown in Figure 11.12.

## Slide 57
Data Transfer Format—10-bit Addressing
Master transmitter transmits to slave receiver with a 10-bit address – shown in Figure
11.16.
Master receiver reads slave transmitter with a 10-bit address – shown in Figure 11.17.
Restart condition is generated in this format.
Combined format – A master sends data to a slave and then reads data from the same
slave. This is shown in Figure 11.18.
Combined format – A master sends data to one slave and then transmit data to another
slave. This format is shown in Figure 11.19.
Combined format – Ten-bit and 7-bit addressing combined in one transfer. This format
is shown in Figure 11.20.

## Slide 60
An Overview of the HCS12 I2C Module
The HCS12 I2C implements a subset of the I2C protocol.
Provides interrupts on start and stop bits in hardware to determine if the I2C bus is free.
Supports only 7-bit addressing
Supports 100 kbps baud rate but requires the user to limit the slew rate to no higher than
100 ns if the 400 kbps baud is to be used.
Limit the maximum bus capacitance to 400 pF for all conditions.
Use PJ7 (SCL) and PJ6 (SDA) pins to support the I2C communication.
Use 5 registers to support its operation:
(a) I2C Control Register (IBCR)
(b) I2C status Register (IBSR)
(c) I2C data I/O register (IBDR)
(d) I2C Frequency Divider Register (IBFD)
(e) I2C Address Register (IBAD)

## Slide 62
Registers for I2C Operation
I2C Address Register (IBAD)
Contains an address to which it will respond when the I2C module is configured as a
slave device.
I2C Data Register (IBDR)
In master transmit mode, a data transfer is started whenever this register is written into.
The most significant bit is shifted out first.
In master receive mode, reading this register initiates the reception of the next byte (the
master sends out 9 clock pulses to shift in data bits and replies with an acknowledge.)

## Slide 63
The I2C Control Register

## Slide 64
The I2C Control Register (continued)
When setting the MS/SL bit from 0 to1, a start signal is generated on the I2C bus
and the master mode is selected.
In the master mode, the Tx/Rx bit should be set according to the type of transfer required.
The TxAK bit specifies the value driven onto the SDA line during data acknowledge
cycles for both master and slave receivers.
I2C module always acknowledges the address matches regardless of the value of TxAK.
Writing a 1 to the RSTA bit will generate a Restart condition on the I2C bus.
The I2C Status Register (IBSR)
When a byte is being transferred, the TCF bit is cleared.
When the I2C is configured as a slave and the address matches then the IAAS
bit will be set .
The IBIF bit will be set under three circumstances:
(a) arbitration lost (IBAL bit is set)
(b) byte transfer complete (TCF bit is set)
(c) addressed as a slave (IAAS bit is set)

## Slide 66
I2C Frequency Divider Register (IBFD)
Four timing requirements to be met:
(a) SCL divider
(b) SDA hold time
(c) SCL hold time for start condition
(d) SCL hold time for stop condition

## Slide 67
The use of the IBFD register
IBC7-IBC6: multiply factor (shown in Table 11.3)
IBC5-IBC3: prescaler divider (shown in Table 11.4)
IBC2-IBC0: shift register tap points (shown in Table 11.5)

## Slide 68
Using Table 11.3, 11.4, and 11.5 is a laborious process.
These three tables can be combined into Table 11.6.
With Table 11.6, finding values to be written into the IBFD register becomes a simple table lookup.
By dividing the intended baud rate into the bus clock, one can locate one or multiple rows in Table 11.6 with the same SCL divider value.
One needs to verify that the SDA hold time, SCL hold time (start), and SCL hold time (stop) all satisfies the timing requirements set out in Table 11.2 before making the selection.

## Slide 69
Example 7: Assuming that the HCS12 is running with a 24 MHz bus clock, compute
the values to be written into the IBFD register to set the baud rate to 100 KHz and 400 KHz.
Solution:
Case 1: Baud Rate = 100 KHz
SCL divider = 24 MHz  100KHz = 240
From Table 11.6,
SDA hold time = 33 E clock cycles = 1.375 ms < 3.45 ms
SCL hold time (start) = 118 E clock cycles = 4.92 ms > 4.0 ms
SCL hold time (stop) = 121 E clock cycles = 5.04 ms > 4.0 ms
The computed value satisfies the timing requirement.
Write the value $1F into the IBFD register at 100 KHz baud rate.
Case 2: Baud rate = 400 KHz
SCL divider = 24 MHz  400KHz = 60
From Table 11.6, the corresponding IBC value is $45.
SDA hold time = 18 E clock cycles = 0.75 ms < 0.9 ms
SCL hold time (start) = 22 E clock cycles = 0.917 ms > 0.6 ms
SCL hold time (stop) = 121 E clock cycles = 1.33 ms > 0.6 ms
The computed value satisfies the timing requirement.
Write the value $45 into the IBFD register at 400 KHz baud rate.

## Slide 70
Configuring the I2C Module
Compute an appropriate value and write it into the IBFD register
Load a value into the IBAD register if the MCU may operate in slave mode.
Set the IBEN bit of the IBCR register to enable I2C module.
Modify the bits of the IBCR register to select master/slave mode, transmit/receive mode,
and interrupt enable mode
; parameters are passed in accumulator A (baud rate) and B (slave address)
openI2C bset IBCR,IBEN ; enable I2C module
staa IBFD ; establish SCL frequency
stab IBAD ; establish I2C module slave address
bclr IBCR,IBIE ; disable I2C interrupt
bset IBCR,IBSWAI ; disable I2C in wait mode
rts
void openI2C (char ibc, char i2c_ID)
{
IBCR |= IBEN; // enable I2C module
IBFD = ibc; // set up I2C baud rate
IBAD = i2c_ID; // set up slave address
IBCR &= ~IBIE; // disable I2C interrupt
IBCR |= IBSWAI; // disable I2C in wait mode
}

## Slide 71
Programming the I2C Module
Generating Start Condition and send Slave ID
sendSlaveID brset IBSR,IBB,* ; wait until I2C bus is free
bset IBCR,TXRX+MSSL ; generate a start condition
staa IBDR ; send out the slave address
brclr IBSR,IBIF,* ; wait for address transmission to complete
movb #IBIF,IBSR ; clear the IBIF flag
rts
void sendSlaveID (char cx)
{
while (IBSR&IBB); // wait until I2C bus is idle
IBCR |= TXRX+MSSL; // generate a start condition
IBDR = cx; // send out the slave address with R/W bit set to 1
while(!(IBSR & IBIF)); // wait for address transmission to complete
IBSR = IBIF; // clear IBIF flag
}

## Slide 72
Instruction sequence to send a byte in accumulator A
staa IBDR
brclr IBSR,IBIF,* ; wait until IBIF flag is set to 1
movb #IBIF,IBSR ; clear the IBIF flag
C statements to send a byte to I2C bus
IBDR = cx; // send out the value cx
while (!(IBSR & IBIF)); // wait until the byte is shifted out
IBSR = IBIF; // clear the IBIF flag
Instruction sequence to read a byte and acknowledge it
bclr IBCR,TXRX+TXAK ; prepare to receive and acknowledge
ldaa IBDR ; a dummy read to trigger 9 clock pulses
brclr IBSR,IBIF,* ; wait until the data byte is shifted in
movb #IBIF,IBSR ; clear the IBIF flag
ldaa IBDR ; place the received byte in A and also initiate the
; next read sequence

## Slide 73
C Statements to read a byte from the I2C bus
IBCR &= ~(TXRX + TXAK); // prepare to receive and acknowledge
dummy = IBDR; // a dummy read
while(!(IBSR & IBIF)); // wait for the byte to shift in
IBSR = IBIF; // clear the IBIF flag
buf = IBDR; // place the received byte in buf and also initiate
// the next read sequence
Instruction Sequence to Read a Byte, Send NACK, and Generate Stop Condition
bclr IBCR,TXRX ; prepare to receive
bset IBCR,TXAK ; perpare to send negative acknowledgement
ldaa IBDR ; dummy read to trigger clock pulses
brclr IBSR,IBIF,* ; wait until the byte is shifted in
movb #IBIF,IBSR ; clear the IBIF flag
bclr IBCR,MSSL ; generate a stop condition
ldaa IBDR ; place the received byte in A

## Slide 74
C Statements to Read a Byte, Send NACK, and generate a Stop Condition
IBCR &= ~TXRX; // prepare to receive
IBCR |= TXAK; // prepare not to acknowledge
dummy = IBDR; // a dummy read to trigger 9 clock pulses
while(!(IBSR & IBIF)); // wait for a byte to shift in
IBSR = IBIF; // clear the IBIF flag
IBCR &= ~MSSL; // generate a stop condition
buf = IBDR; // place the received byte in buf

## Slide 75
I2C Data Transfer in Slave Mode
After reset and stop condition, the I2C module is in slave mode.
Once in slave mode, the I2C module waits for a start condition to come.
Following the start condition, eight bits are shifted into the IBAD register.
The value of the upper 7 bits of the received byte is compared with the IBAD register.
If the address matches, the following events occur:
(a) The bit 0 of the address byte is copied into the SRW bit of the IBSR register.
(b) The IAAS bit is set to indicate the address match.
(c) An ACK pulse is generated regardless of the value of the TXAK bit.
(d) The IBIF bit is set

## Slide 76
Instruction sequence to make sure the address match and take appropriate action
brset IBSR,IAAS,addr_match ; is address matched?
…
addr_match brclr IBSR,SRW,slave_rd
bset IBCR,TXRX ; prepare to transmit data
movb tx_buf,IBDR ; place data in IBDR to wait for SCL to shift it out
brclr IBSR,IBIF,* ; wait for data to be shifted out
…
slave_rd bclr IBCR,TXAK+TXRX ; prepare to receive and send ACK
brclr IBSR,IBIF,* ; wait for data byte to shift in
movb #IBIF,IBSR ; clear the IBIF flag
movb IBDR,rcv_buf ; save the received data

## Slide 77
Exercise 8: Digital Thermometer and Thermostat DS1631A
Mainly used to warn the possible overheat of the embedded system to prevent system
failure.
When the ambient temperature exceeds the trip point, the DS1631A asserts the TOUT
signal.

## Slide 78
DS1631A converts temperature into 9-, 10-, 11-, or 12-bit readings over a range of
-55oC to 125oC.
TOUT is asserted whenever the converted ambient temperature is equal to or higher than
the value stored in the TH register.
Once asserted, the TOUT output will stay high until the temperature drops below the value
stored in the TL register.
Negative temperatures are represented in twos complement format.
DS1631A Registers
Config, TH, TL, and Temperature are DS1631A internal registers.
The Config register is 8-bit.
The Config register can be read from and written into.
TH, TL, and Temperature registers are 16-bit.

## Slide 80
Converting the Conversion Result to temperature
The conversion result cannot be higher than 0x7D00 or lower than 0xC900.
A sample of temperature reading is shown in Table 11.8 .
Positive Conversion Result
Step 1
Truncate the lowest four bits.
Step 2
Divide the upper 12 bits by 16.
Negative Conversion Result
Step 1
Compute the twos complement of the conversion result.
Step 2
Truncate the lowest 4 bits.
Step 3
Divide the upper 12 bits of the twos complement of the conversion result by 16.

## Slide 81
DS1631A Command Set
Start Convert T (0x51)
Stop Convert T (0x22)
Read Temperature (0xAA)
Access TH (0xA1)
Access TL (0xA2)
Access Config (0xAC)
Software POR (0x54)
Circuit Connection

## Slide 82
DS1631A Control Byte (Device ID)
Example 8.1: Write a function to configure the DS1631A in Figure 11.34 to operate in continuous conversion mode and set the TOUT polarity to active high. Assume that the I2C has only one master and there is no possibility in getting bus collision.
Solution:
Call the openDS1631 function on the next slide with the configuration byte of 0xE0:
ldab #$E0
jsr openDS1631

## Slide 83
openDS1631 ldaa #$92
jsr sendSlaveID
brclr IBSR,RXAK,openOK0 ; did DS1631A acknowledge?
ldab #$FF ; return error code -1
rts
openOK0 movb #$AC,IBDR ; send the "Access Config" command
brclr IBSR,IBIF,*
movb #IBIF,IBSR ; clear the IBIF flag
brclr IBSR,RXAK,openOK1 ; did DS1316A acknowledge?
ldab #$FF
rts
openOK1 stab IBDR ; sends configuration data
brclr IBSR,IBIF,* ; wait until the byte has been shifted out
movb #IBIF,IBSR ; clear the IBIF flag
brclr IBSR,RXAK,openOK2 ; did DS1316A acknowledge?
ldab #$FF
rts
openOK2 bclr IBCR,MSSL ; generate a stop condition
ldab #0 ; normal return code
rts

## Slide 84
C function to initialize the DS1631A
char openDS1631(char cy)
{
sendSlaveID(0x92); // generate a start condition and send ID
if (IBSR & RXAK)
return -1; // error code when DS1631 did not acknowledge
IBDR = 0xAC; // send command "Access Config"
while(!(IBSR & IBIF));
IBSR = IBIF; // clear the IBIF flag
if (IBSR & RXAK)
return -1; // error code when DS1631 did not acknowledge
IBDR = cy; // send configuration byte
while(!(IBSR & IBIF));
IBSR = IBIF;
if (IBSR & RXAK)
return -1; // error code when DS1631 did not acknowledge
IBCR &= ~MSSL; // generate a stop condition
return 0; // normal return code
}

## Slide 85
Example 8.2: Write a function to command the DS1631A to start temperature conversion.
Solution:

## Slide 86
Example 8.2: Write a function to command the DS1631A to start temperature conversion.
Solution:
startConv ldaa #$92
jsr sendSlaveID ; generate a start condition and send DS1631's ID
brclr IBSR,RXAK,startOK0 ; did DS1631A acknowledge?
ldab #$FF ; return error code -1
rts
startOK0 movb #$51,IBDR ; send "Start Convert T" command
brclr IBSR,IBIF,* ; wait until the byte is shifted out
movb #IBIF,IBSR ; clear the IBIF flag
brclr IBSR,RXAK,startOK1 ; did DS1631A acknowledge?
ldab #$FF
rts
startOK1 bclr IBCR,MSSL ; generate a stop condition
ldab #0 ; normal return code
rts

## Slide 87
Example 8.2: Write a function to command the DS1631A to start temperature conversion.
Solution:

## Slide 88
Example 8.3: Write a function to set the high thermostat temperature. The upper and
lower bytes of the high thermostat temperatures are passed in stack.
Solution:

## Slide 89
Example 8.3: Write a function to set the high thermostat temperature. The upper and
lower bytes of the high thermostat temperatures are passed in stack. (the highest temp to be accepted)
Solution:
THhi equ 2
THlo equ 3
setTH ldaa #$92
jsr sendSlaveID
brclr IBSR,RXAK,setTHok1 ; did DS1631A acknowledge?
ldab #$FF ; return error code -1
rts
setTHok1 movb #$A1,IBDR ; send out access TH command */
brclr IBSR,IBIF,* ; wait until command is shifted out
movb #IBIF,IBSR ; clear IBIF flag
brclr IBSR,RXAK,setTHok2 ; did DS1631A acknowledge?
ldab #$FF
rts
setTHok2 ldaa THhi,sp ; get the upper byte of TH from stack
staa IBDR ; send out TH high byte
brclr IBSR,IBIF,*
movb #IBIF,IBSR ; clear the IBIF flag
brclr IBSR,RXAK,setTHok3 ; did DS1631A acknowledge?
ldab #$FF
rts

## Slide 90
setTHok3 ldaa THlo,sp ; get the lower byte of TH from stack
staa IBDR
brclr IBSR,IBIF,*
movb #IBIF,IBSR ; clear the IBIF flag
brclr IBSR,RXAK,setTHok4 ; did DS1631A acknowledge?
ldab #$FF
rts
setTHok4 bclr IBCR,MSSL ; generate the stop condition
ldab #0 ; normal return code
rts

## Slide 92
Example 8.4 Write a function to read the Config register from the DS1631A and return its value in accumulator B.

## Slide 93
Example 8.4 Write a function to read the Config register from the DS1631A and return its value in accumulator B.

## Slide 94
Example 8.4 Write a function to read the Config register from the DS1631A and return its value in accumulator B.

## Slide 95
Example 8.4 Write a function to read the Config register from the DS1631A and return its value in accumulator B.

## Slide 96
Example 8.5: Write a subroutine to read the converted temperature and return the upper and lower
bytes in double accumulator D. Assume that the temperature conversion has been started but this
function needs to make sure that the converted temperature value is resulted from the most recent
“Start Convert T” command.

## Slide 97
readTemp ldx #0 ; initialize return error code
rdLoop jsr readConf ; is temperature conversion done yet?
cmpb #-1 ; is there any error?
beq rdErr ; "
andb #$80 ; check DONE bit
bpl rdLoop ; conversion not done yet?
ldaa #$92 ; generate a start condition and send out
jsr sendSlaveID ; the DS1631A ID
brclr IBSR,RXAK,rdTempok1 ; did DS1631A acknowledge?
ldx #-1
rts
rdTempok1 movb #$AA,IBDR ; sends "Read Temperature command"
brclr IBSR,IBIF,* ;
movb #IBIF,IBSR
brclr IBSR,RXAK,rdTempok2 ; did DS1631A acknowledge?
ldx #-1
rts
rdTempok2 bset IBCR,RSTA ; generate a restart condition
movb #$93,IBDR ; send DS1631A's ID with R/W set to 1
brclr IBSR,IBIF,*
movb #IBIF,IBSR
brclr IBSR,RXAK,rdTempok3 ; did DS1631A acknowledge?
ldx #-1
rts

## Slide 98
rdTempok3 bclr IBCR,TXRX+TXAK ; prepare to receive and ACK
ldaa IBDR ; perform a dummy read
brclr IBSR,IBIF,* ; wait for high byte of temperature to shift in
movb #IBIF,IBSR
bset IBCR,TXAK ; prepare send NACK for the last read
ldaa IBDR ; place the high byte of Temperature in A
brclr IBSR,IBIF,* ; wait for the low byte read to complete
movb #IBIF,IBSR ; clear the IBIF flag
bclr IBCR,MSSL ; generate a stop condition
ldab IBDR ; place the low byte of temperature in B
ldx #0 ; correct return code
rts
rdErr ldx #-1
rts

## Slide 99
Homework:
Write the C variant for Example 8.5 
For the circuit shown in Figure 11.34, add a LED to HCS12 and set the high-temperature trip point to 50°C. Whenever temperature reaches 50°C or higher, turn on the LED until the temperature drops down to 23°C. Please write the scheme, code and explanations.
void main (void)
{
openI2C(…,…); // set I2C baud rate to 100 KHz
openDS1631(…); // configure DS1631 to perform 12-bit DTA conversion
// continuously at set TOUT to be idle high
setTH(…,…); // set TH to 50oC
setTL(…,…); // set TL to 23oC
startConv(); // start the DS1631A temperature conversion
// LED specific operations or functions’ calling …
while(1); // wait forever
}

## Slide 100: Content
What is Serial Peripheral Interface (SPI)?
The HCS12 SPI Modules
SPI Related Registers
The I2C Protocol
An Overview of the HCS12 I2C Module